The following are trademarks of Intel Corporation and its affiliates and may be used only to identify Intel products: BXP, CREDIT, i, ICE, ICS, im, insite, Intel, INTEL, Intelevision, Intellec, iSBC, iSBX, Library Manager, MCS, MAIN MULTIMODULE, Megachassis, Micromap, MULTIBUS, Plug-A-Bubble, PROMPT, Promware, RMX, UPI, µScope, System 2000, Micromainframe, and the combination of MCS, ICE, iSBC, iRMX or iCS and a numerical suffix.

			Instruction Code					Flags
Mnemonic	Function	Description	D7	D6	D5	D4	D3	D2	D1	D0	Cycles	Bytes	C	AC	F0	F1
Data Moves
MOV A, = data	(A) ← data	Move immediate the specified data into the Accumulator.	0 d7	0 d6	1 d5	0 d4	0 d3	0 d2	1 d1	1 d0	2	2
MOV A, Rr	(A) ← (Rr); r = 0 – 7	Move the contents of the designated register into the Accumulator.	1	1	1	1	1	r	r	r	1	1
MOV A, @ Rr	(A) ← ((Rr)); r = 0 – 1	Move indirect the contents of data memory location into the Accumulator.	1	1	1	1	0	0	0	r	1	1
MOV A, PSW	(A) ← (PSW)	Move contents of the Program Status Word into the Accumulator.	1	1	0	0	0	1	1	1	1	1
MOV Rr, = data	(Rr) ← data; r = 0 – 7	Move immediate the specified data into the designated register.	1 d7	0 d6	1 d5	1 d4	1 d3	r d2	r d1	r d0	2	2
MOV Rr, A	(Rr) ← (A); r = 0 – 7	Move Accumulator contents into the designated register.	1	0	1	0	1	r	r	r	1	1
MOV @ Rr, A	((Rr)) ← (A); r = 0 – 1	Move indirect Accumulator contents into data memory location.	1	0	1	0	0	0	0	r	1	1
MOV @ Rr, = data	((Rr)) ← data; r = 0 – 1	Move immediate the specified data into data memory.	1 d7	0 d6	1 d5	1 d4	0 d3	0 d2	0 d1	r d0	2	2
MOV PSW, A	(PSW) ← (A)	Move contents of Accumulator into the Program Status Word.	1	1	0	1	0	1	1	1	1	1
MOVP A, @ A	(PC 0 – 7) ← (A) (A) ← ((PC))	Move data in the current page into the Accumulator.	1	0	1	0	0	0	1	1	2	1
MOVP3 A, @ A	(PC 0 – 7) ← (A) (PC 8 – 10) ← 011 (A) ← ((PC))	Move Program data in Page 3 into the Accumulator.	1	1	1	0	0	0	1	1	2	1
MOVX A, @ Rr	(A) ← ((Rr)); r = 0 – 1	Move indirect the contents of external data memory into the Accumulator.	1	0	0	0	0	0	0	r	2	1
MOVX @ Rr, A	((Rr)) ← (A); r = 0 – 1	Move indirect the contents of the Accumulator into external data memory.	1	0	0	1	0	0	0	r	2	1
XCH A, Rr	(A) ⇄ (Rr); r = 0 – 7	Exchange the Accumulator and designated register's contents.	0	0	1	0	1	r	r	r	1	1
XCH A, @ Rr	(A) ⇄ ((Rr)); r = 0 – 1	Exchange indirect contents of Accumu­lator and location in data memory.	0	0	1	0	0	0	0	r	1	1
XCHD A, @ Rr	(A 0 – 3) ⇄ ((Rr)(0 – 3)) r = 0 – 1	Exchange indirect 4-bit contents of Accumulator and data memory.	0	0	1	1	0	0	0	r	1	1
Flags
CPL C	(C) ← NOT (C)	Complement content of carry bit.	1	0	1	0	0	1	1	1	1	1	•
CPL F0	(F0) ← NOT (F0)	Complement content of Flag F0.	1	0	0	1	0	1	0	1	1	1			•
CPL F1	(F1) ← NOT (F1)	Complement content of Flag F1.	1	0	1	1	0	1	0	1	1	1				•
CLR C	(C) ← 0	Clear content of carry bit to 0.	1	0	0	1	0	1	1	1	1	1	•
CLR F0	(F0) ← 0	Clear content of Flag 0 to 0.	1	0	0	0	0	1	0	1	1	1			•
CLR F1	(F1) ← 0	Clear content of Flag 1 to 0.	1	0	1	0	0	1	0	1	1	1				•

Table 5. D.C. Specification for Programming 8748H/8749H
Symbol	Parameter	Min	Max	Unit	Test Conditions
VDDH	VDD Program Voltage High Level	20.5	21.5	V
VDDL	VDD Voltage Low Level	4.75	5.25	V
VPH	PROG Program Voltage High Level	17.5	18.5	V
VPL	PROG Voltage Low Level	4.0	VCC	V
VEAH	EA Program or Verify Voltage High Level	17.5	18.5	V
IDD	VDD High Voltage Supply Current		20.0	mA
IPROG	PROG High Voltage Supply Current		1.0	mA
IEA	EA High Voltage Supply Current		1.0	mA

TA = 25 °C; VCC = 5 V ±5%; VDD = 21 V ±5%
Figure 19. 8048AH and 8049AH Logic Symbol
Figure 17. Power Down Sequence
Figure 15.
Figure 14. 8048AH/8049AH Instruction Timing Diagram
Figure 13. MCS-48 Timing Generation and Cycle Timing
Table 2. Baud Rate Generation
Frequency (MHz)		TCY	T0 Prr(1/5 TCY)	Timer Prescaler (32 TCY)
	4 6 8 11	3.75 µs 2.50 µs 1.88 µs 1.36 µs	750 ns 500 ns 375 ns 275 ns	120 µs 80 µs 60.2 µs 43.5 µs
Baud Rate	4 MHz Timer Counts + Instr. Cycles	6 MHz Timer Counts + Instr. Cycles	8 MHz Timer Counts + Instr. Cycles	11 MHz Timer Counts + Instr. Cycles
110	75 + 24 Cycles .01% Error	113 + 20 Cycles .01% Error	151 + 3 Cycles .01% Error	208 + 28 Cycles .01% Error
300	27 + 24 Cycles .1% Error	41 + 21 Cycles .03% Error	55 + 13 Cycles .01% Error	76 + 18 Cycles .04% Error
1200	6 + 30 Cycles .1% Error	10 + 13 Cycles .1% Error	12 + 27 Cycles .06% Error	19 + 4 Cycles .12% Error
1800	4 + 20 Cycles .1% Error	6 + 30 Cycles .1% Error	9 + 7 Cycles .17% Error	12 + 24 Cycles .12% Error
2400	3 + 15 Cycles .1% Error	5 + 6 Cycles .4% Error	6 + 24 Cycles .29% Error	9 + 18 Cycles .12% Error
4800	1 + 23 Cycles 1.0% Error	2 + 19 Cycles .4% Error	3 + 14 Cycles .74% Error	4 + 25 Cycles .12% Error

Figure 12. Timer/Event Counter
Figure 11. Interrupt Logic

Grokking the MCS-48 System

Version 3.5, May 2021

Preface

This document came into existence as the effort to collect and maintain the information about the MCS-48 microcontroller family I have access to.
The collected paperwork consists of several copied sheets from Intel databooks that age over time, slowly fading away. In addition, the resources in electronic form for this micro­controller family were never complete nor exhaustive. As nowadays, not everyone is lucky enough to have access to these old, big databooks, this document intends to transport all the knowledge necessary to work with these grandfathers.
Please note that this document does not claim correctness of the contained information. Nor should you ever use it as the only reference for building critical applications.

Five separate sources contributed to this document:
- Two different versions of the "MCS-48TM Microcomputer User's Manual"
  The chapter "The Expanded MCS-48TM System" was found in a 1978's copy of the User's Manual while the chapter "The Single Component MCS®-48 System" was probably part of a later revision of the User's Manual.
- Das 8039, 8048, 8748 Brevier
  H. Weidner, Braunschweig
  The first part of this booklet is a translation of "The Single Component MCS®-48 System" into the German language while the second part gives a very detailed description of the family's instruction set.
- HMOS Single-Component 8-Bit Microcomputer
  Intel Corporation, August 1982, Order Number 210677-001
  A 9-page datasheet with an excellent instruction set table.
- Some scanned pages with details about the 8243, apparently from an old Intel databook.
- A set of copied pages containing the 8245 product specification. The second page of the character set is missing.

October 2006

Arnim Läuger
mailto: arnim.laeuger <at> gmx.net

HMOS Single-Component 8-Bit Microcomputer

• High Performance HMOS	• Reduced Power Consumption
• Interval Timer/Event Counter	• Compatible with 8080/8085 Peripherals
• Two Single Level Interrupts	• Easily Expandable Memory and I/O
• Single 5-Volt Supply	• Up to 1.36 μs Instruction Cycle
• Over 96 Instructions; 90% Single Byte	All Instructions 1 or 2 Cycles

The Intel MCS®-48 family are totally self-sufficient, 8-bit parallel computers fabricated on single silicon chips using Intel's advanced N-channel silicon gate HMOS process.
The family contains 27 I/O lines, an 8-bit timer/counter and on-board oscillator/clock circuits. For systems that require extra capability, the family can be expanded using MCS®-80/MCS®-85 peripherals.
To minimize development problems and provide maximum flexibility, a logically and functionally pin-compati­ble version of the ROM devices with UV-erasable user-programmable EPROM program memory is available with minor differences.
These microcomputers are designed to be efficient controllers as well as arithmetic processors. They have extensive bit handling capability as well as facilities for both binary and BCD arithmetic. Efficient use of pro­gram memory results from an instruction set consisting mostly of single byte instructions and no instructions over 2 bytes in length.
Device	Internal Memory				RAM Standby
8050AH	4K x 8	ROM	256 x 8	RAM	yes
8049H	2K x 8	ROM	128 x 8	RAM	yes
8048H	1K x 8	ROM	64 x 8	RAM	yes
8040AHL	none		256 x 8	RAM	yes
8039HL	none		128 x 8	RAM	yes
8035HL	none		64 x 8	RAM	yes
8749H	2K x 8	EPROM	128 x 8	RAM	yes
8748H	1K x 8	EPROM	64 x 8	RAM	yes

Figure 1.
Block Diagram
Figure 2.
Logic Symbol
Figure 3.
Pin Configuration
# INTRODUCTION
Sections 2 through 5 describe in detail the functional characteristics of the 8748H and 8749H EPROM, 8048AH/8049AH/8050AH ROM and 8035AHL/ 8039AHL/8040AHL CPU single component micro­computers. Unless otherwise noted, details within these sections apply to all versions. This chapter is limited to those functions useful in single-chip implementations of the MCS®-48. The Chapter on the Expanded MCS®-48 System discusses functions which allow expansion of program memory, data memory, and input output capa­bility.
# ARCHITECTURE
The following sections break the MCS-48 Family into functional blocks and describe each in detail. The follow­ing description will use the 8048AH as the representative product for the family. See 4.
## Arithmetic Section
The arithmetic section of the processor contains the basic data manipulation functions of the 8048AH and can be divided into the following blocks:
- Arithmetic Logic Unit (ALU)
- Accumulator
- Carry Flag
- Instruction Decoder
In a typical operation data stored in the accumulator is combined in the ALU with data from another source on the internal bus (such as a register or I/O port) and the result is stored in the accumulator or another register.
The following is more detailed description of the function of each block.
#### INSTRUCTION DECODER
The operation code (op code) portion of each program instruction is stored in the Instruction Decoder and is con­verted to outputs which control the function of each of the blocks of the Arithmetic Section. These lines control the source of data and the destination register as well as the function performed in the ALU.
#### ARITHMETIC LOGIC UNIT
The ALU accepts 8-bit data words from one or two sources and generates an 8-bit result under control of the Instruction Decoder. The ALU can perform the fol­lowing functions:
- Add With or Without Carry
- AND, OR, Exclusive OR
- Increment/Decrement
- Bit Complement
- Rotate Left, Right
- Swap Nibbles
- BCD Decimal Adjust
If the operation performed by the ALU results in a value represented by more than 8 bits (overflow of most sig­nificant bit), the Carry Flag is set in the Program Status Word.
#### ACCUMULATOR
The accumulator is the single most important data register in the processor, being one of the sources of input to the ALU and often the destination of the result of operations performed by the ALU. Data to and from I/O ports and memory also normally passes through the accumulator.
## Program Memory
Resident program memory consists of 1024, 2048 or 4096 words eight bit wide which are addressed by the program counter. In the 8748H and the 8749H this memory is user programmable and erasable EPROM; in the 8048AH/ 8049AH/8050AH the memory is ROM which is mask programmable at the factory. The 8035AHL/8039AHL/ 8040AHL has no internal program memory and is used with external memory devices. Program code is com­pletely interchangeable among the various versions. To access the upper 2K of program memory in the 8050AH and other MCS-48 devices, a select memory bank and a JUMP or CALL instruction must be executed to cross the 2K boundary.
There are three locations in Program Memory of special importance as shown in 5.
LOCATION 0
Activating the Reset line of the processor causes the first instruction to be fetched from location 0.
LOCATION 3
Activating the Interrupt input line of the processor (if interrupt is enabled) causes a jump to subroutine at lo­cation 3.
LOCATION 7
A timer/counter interrupt resulting from timer counter overflow (if enabled) causes a jump to subroutine at loca­tion 7.
Therefore, the first instruction to be executed after ini­tialization is stored in location 0, the first word of an external interrupt service subroutine is stored in location 3 and the first word of a timer/counter service routines is stored in location 7. Program memory can be used to

Figure 4: 8748H/8048H/8749AH/8050AH Block Diagram
store constants as well as program instructions. Instruc­tions such as MOVP and MOVP3 allow easy access to data "lookup" tables.
Figure 5. Program Memory Map
## Data Memory
Resident data memory is organized as 64, 128 or 256 by 8-bits wide in the 8048AH, 8049AH and 8058AH. All locations are indirectly addressable through either of two RAM Pointer Registers which reside at address 0 and 1 of the register array. In addition, as shown in 6, the first 8 locations (0-7) of th array are designated as working registers and are directly addressable by several instructions. Since these registers are more easily ad­dressed, they are usually used to store frequently accessed intermediate results. The DJNZ instruction makes very efficient use of the working registers as program loop counters by allowing the programmer to decrement and test the register in a single instruction.
By executing a Register Bank Switch instruction (SEL RB), RAM locations 24-31 are designated as the working registers in place of locations 0-7 and are then directly addressable. This second bank of working registers may be used as an extension of the first bank or reserved for use during interrupt service subroutines allowing the re­gisters of Bank 0 used in the main program to be instantly "saved" by a Bank Switch. Note that if this second bank is not used, locations 24-31 are still addressable as general purpose RAM. Since the two RAM pointer Registers R0 and R1 are a part of the working register array, bank switch effectively creates two more pointer registers (R0/ and R1/) which can be used with R0 and R1 to easily access up to four separate working areas in RAM at one time. RAM locations 8-23 also serve a dual role in that they contain the program counter stack as explained in Section 2.6. These locations are addressed by the Stack Pointer during subroutine calls as well as by RAM Pointer Registers R0 and R1. If the level of subroutine nesting is less than 8, all stack registers are not required and can be used as general purpose RAM locations. Each level of subroutine nesting not used provides the user with two additional RAM locations.

Figure 6. Data Memory Map

Figure 7. "Quasi-bidirectional" Port Structure
## Input/Output
The 8048AH has 27 lines which can be used for input or output functions. These lines are grouped as 3 ports of 8 lines each which serve as either inputs, outputs or bidi­rectional ports and 3 "test" inputs which can alter program sequences when tested by conditional jump instructions.
#### PORTS 1 AND 2
Ports 1 and 2 are each 8 bits wide and have identical characteristics. Data written to these ports is statically latched and remains unchanged until rewritten. As input ports these lines are non-latching, i. e., inputs must be present until read by an input instruction. Inputs are fully TTL compatible and outputs will drive one standard TTL load.
The lines of ports 1 and 2 are called quasi-bidirectional because of a special output circuit structure which allows each line to serve as an input and output or both even though outputs are statically latched. 7 shows the circuit configuration in detail. Each line is continu­ously pulled to VCC through a resistive device of relatively high impedance.
This pullup is sufficient to provide the source current for a TTL high level yet can be pulled low by a standard TTL gate thus allowing the same pin to be used for both input and output. To provide fast switching times in a "0" to "1" transition a relatively low impedance device is switched in momentarily (≈ 1/5 of a machine cycle) whenever a "1" is written to the line. When a "0" is written to the line, a low impedance device overcomes the light pullup and provides TTL current sinking capability. Since the pulldown transistor is a low impedance device a "1" must first be written to any line which is to be used as an input. Reset initializes all lines to the high impedance "1" state.
It is important to note that the ORL and the ANL are read/ write operations. When executed, the μC "reads" the port, modifies the data according to the instruction, then "writes" the data back to the port. The "writing" (es­sentially an OUTL instruction) enables the low impedance pull-up momentarily again even if the data was un­changed from a "1". This specifically applies to configurations that have inputs and outputs mixed together on the same port. See also section 8 in the Expanded MCS-48 System chapter.
#### BUS
Bus is also an 8-bit port which is a true bidirectional port with associated input and output strobes. If the bidirec­tional feature is not needed, Bus can serve as either a statically latched output port or non-latching input port. Input and output lines on this port cannot be mixed however.
As a static port, data is written and latched using the OUTL instruction and inputted using the INS instruction. The INS and OUTL instructions generate pulses on the corresponding RD' and WR' output strobe lines; however, in the static port mode they are generally not used. As a bidirectional port the MOVX instructions are used to read and write the port. A write to the port generates a pulse on the WR' output line and output data is valid at the trailing edge of WR'. A read of the port generates a pulse on the RD' output line and input data must be valid at the trailing edge of RD'. When not being written or read, the BUS lines are in a high impedance state. See also sections 7 and 8 in the Expanded MCS-48 System chapter.
## Test and INT Inputs
Three pins serve as inputs and are testable with the con­ditional jump instructions. These are T0, T1, and INT'. These pins allow inputs to cause program branches without the necessity to load an input port into the accu­mulator. The T0, T1, and INT' pins have other possible functions as well. See the pin description in Section 3.
## Program Counter and Stack
The Program Counter is an independent counter while the Program Counter Stack is implemented using pairs of registers in the Data Memory Area. Only 10, 11 or 12 bits of the Program Counter are used to address the 1024, 2048 or 4096 words of on-board program memory of the 8048AH, 8049AH or 8050AH, while the most significant bits can be used for external Program Memory fetches. See 8. The Program Counter is initialized to zero by activating the Reset line.
An interrupt or CALL to a subroutine causes the contents of the program counter to be stored in one of the 8 register pairs of the Program Counter Stack as shown in 9. The pair to be used is determined by a 3-bit Stack Pointer which is part of the Program Status Word (PSW).
Figure 8. Program Counter

Data RAM locations 8-23 are available as stack registers and are used to store the Program Counter and 4 bits of PSW as shown in 9. The Stack Pointer when initialized to 000 points to RAM location 8 and 9. The first subroutine jump or interrupt results in the program counter contents being transferred to locations 8 and 9 of the RAM array. The stack pointer is then incremented by one to point to locations 10 and 11 in anticipation of another CALL. Nesting of subroutines within subroutines can continue up to 8 times without overflowing the stack. If overflow does occur, the deepest address stored (loca­tions 8 and 9) will be overwritten and lost since the stack pointer overflows from 111 to 000. It also underflows from 000 to 111.
Figure 9. Program Counter Stack
The end of a subroutine, which is signaled by a return instruction (RET or RETR), causes the Stack Pointer to be decremented and the contents of the resulting register pair to be transferred to the Program Counter.
## Program Status Word
An 8-bit status word which can be loaded to and from the accumulator exists called the Program Status Word (PSW). 10 shows the information available in the word. The Program Status Word is actually a collection of flip-flops throughout the machine which can be read or written as a whole. The ability to write the PSW allows for easy restoration of machine status after a power down sequence.
The upper four bits of PSW are stored in the Program Counter Stack with every call to subroutine or interrupt vector and are optionally restored upon return with the RETR instruction. The RET return instruction does not update PSW.
Figure 10. Program Status Word (PSW)
The PSW bit definitions are as follows:
Bits 0-2:	Stack Pointer bits (S0, S1, S2)
Bit 3:	Not used ("1" level when read)
Bit 4:	Working Register Bank Switch Bit (BS) 0 = Bank 0 1 = Bank 1
Bit 5:	Flag 0 bit (F0) user controlled flag which can be complemented or cleared and tested with the conditional jump instruction JF0.
Bit 6:	Auxiliary Carry (AC) carry bit generated by an ADD instruction and used by the decimal adjust instruction DA A.
Bit 7:	Carry (CY) carry flag which indicates that the previous operation has resulted in overflow of the accumulator.

## Conditional Branch Logic
The conditional branch logic within the processor enables several conditions internal and external to the processor to be tested by the user program. By using the conditional jump instruction the conditions that are listed in 1 can affect a change in the sequence of the program execution.
Table 1
Device Testable	Jump Condition (Jump On)
		not all
Accumulator	All zeros	zeros
Accumulator Bit	---	1
Carry Flag	0	1
User Flags (F0, F1)	---	1
Timer Overflow Flag	---	1
Test Inputs (T0, T1)	0	1
Interrupt Input (INT)	0	---

## Interrupt
An interrupt sequence is initiated by applying a low "0" level input to the INT' pin. Interrupt is level triggered and active low to allow "WIRE ORing" of several interrupt sources at the input pin. 11 shows the interrupt logic of the 8048AH. The interrupt line is sampled every instruction cycle and when detected causes a "call to subroutine" at location 3 in program memory as soon as all cycles of the current instruction are complete. On 2-cycle instructions the interrupt line is sampled on the 2nd cycle only. INT' must be held low for at least 3 machine cycles to ensure proper interrupt operations. As in any CALL to subroutine, the Program Counter and Program Status word is saved in the stack. For a description of this operation see the previous section, Program Counter and Stack. Program Memory location 3 usually contains an unconditional jump to an interrupt service subroutine elsewhere in program memory. The end of an interrupt service subroutine is signaled by the execution of a Return and Restore Status instruction RETR. The interrupt system is single level in that once an interrupt is detected all further interrupt requests are ignored until execution of an RETR reenables the interrupt input logic. This occurs at the beginning of the second cycle of the RETR instruction. This sequence holds true also for an internal interrupt generated by timer overflow. If an internal timer/counter generated interrupt and an external source will be recognized at the same time, the external source will be recognized. See the following Timer/Counter section for a description of timer interrupt. If needed, a second external interrupt can be created by enabling the timer/counter interrupt, loading FFH in the Counter (one less than terminal count) and enabling the event counter mode. A "1" to "0" transition on the T1 input will then cause an interrupt vector to location 7.
#### INTERRUPT TIMING
The interrupt input may be enabled or disabled under Program Control using the EN I and DIS I instructions. Interrupts are disabled by Reset and remain so until enabled by the user's program. An interrupt request must be removed before the RETR instruction is executed upon return from the service subroutine otherwise the processor will re-enter the service routine immediately. Many peripheral devices prevent this situation by resetting their interrupt request line whenever the processor accesses (Reads or Writes) the peripheral's data buffer register. If the interrupt device does not require access by the processor, one output line of the 8048AH may be des­ignated as an "interrupt acknowledge" which is activated by the service subroutine to reset the interrupt request. The INT' pin may also be tested using the conditional jump instruction JNI. This instruction may be used to detect the presence of a pending interrupt before interrupts are enabled. If interrupt is left disabled, INT' may be used as another test input like T0 and T1.
## Timer/Counter
The 8048AH contains a counter to aid the user in counting external events and generating accurate time delays with­out placing a burden on the processor for these functions. In both modes the counter operation is the same, the only difference being the source of the input to the counter. The timer/event counter is show in 12.
#### COUNTER
The 8-bit binary counter is presettable and readable with the MOV instructions which transfer the contents of the accumulator to the counter and vice versa. The counter content may be affected by Reset and should be initialized by software. The counter is stopped by a Reset or STOP TCNT instruction and remains stopped until started as a timer by a STRT T instruction or as an event counter by a STRT CNT instruction. Once started, the counter will increment to this maximum count (FF) and overflow to zero continuing its count until stopped by a STOP TCNT instruction or Reset.
The increment from maximum count to zero (overflow) results in the setting of an overflow flag flip-flop and in the generation of an interrupt request. The state of the overflow flag is testable with the conditional jump instruc­tion JTF. The flag is reset by executing a JTF or by Reset. The interrupt request is stored in a latch and then ORed with the external interrupt input INT. The timer interrupt may be enabled or disabled independently of external in­terrupt by the EN TCNTI and DIS TCNTI instructions. If enabled, the counter overflow will cause a subroutine call to location 7 where the timer or counter service routine may be stored.
If timer and external interrupts occur simultaneously, the external interrupt will be recognized and the Call will be to location 3. Since the timer interrupt is latched it will remain pending until the external device is serviced and immediately be recognized upon return from the service routine. The pending timer interrupt is reset by the Call to location 7 or may be removed by executing a DIS TCNTI instruction.
#### AS AN EVENT COUNTER
Execution of a START CNT instruction connects the T1 input pin to the counter input and enables the counter. The T1 input is sampled at the beginning of state 3 or in later MCS-48 devices in state time 4. Subsequent high to low transitions on T1 will cause the counter to increment. T1 must be held low for at least 1 machine cycle to ensure it won't be missed. The maximum rate at which the counter may be incremented is once per three instruction cycles (every 5.7 µsec when using an 8 MHz crystal) --- there is no minimum frequency. T1 input must remain high for at least 1/5 machine cycle after each transition.
#### AS A TIMER
Execution of a START T instruction connects an internal clock to the counter input and enables the counter. The internal clock is derived by passing the basic machine cycle clock through a ÷ 32 prescaler. The prescaler is reset during the START T instruction. The resulting clock increments the counter every 32 machine cycles. Various delays from 1 to 256 counts can be obtained by presetting the counter and detecting overflow. Times longer than 256 counts may be achieved by accumulating multiple overflows in a register under software control. For time resolution less than 1 count an external clock can be applied to the T1 input and the counter operated in the event counter mode. ALE divided by 3 or more can serve as this external clock. Very small delays or "fine tuning" of larger delays can be easily accomplished by software delay loops.
Often a serial link is desirable in an MCS-48 family mem­ber. 2 lists the timer counts and cycles needed for a specific baud rate given a crystal frequency.
## Clock and Timing Circuits
Timing generation for the 8048AH is completely self con­tained with the exception of a frequency reference which can be XTAL, ceramic resonator or external clock source. The Clock and Timing circuitry can be divided into the following functional blocks.
#### OSCILLATOR
The on-board oscillator is a high gain parallel resonant circuit with a frequency range of 1 to 11 MHz. The X1 external pin is the input to the amplifier stage while X2 is the output. A crystal or ceramic resonator connected between X1 and X2 provides the feedback and phase shift required for oscillation. If an accurate frequency reference is not required, ceramic resonator may be used in place of the crystal.
For accurate clocking, a crystal should be used. An ex­ternally generated clock may also be applied to X1—X2 as the frequency source. See the data sheet for more information.
#### STATE COUNTER
The output of the oscillator is divided by 3 in the State Counter to create a clock which defines the state times of the machine (CLK). CLK can be made available on the external pin T0 by executing an ENT0 CLK instruction. The output of CLK on T0 is disabled by Reset of the processor.
#### CYCLE COUNTER
CLK is then divided by 5 in the Cycle Counter to provide a clock which defines a machine cycle consisting of 5 machine states as shown in 13. 14 shows the different internal operations as divided into the machine states. This clock is called Address Latch Enable (ALE) because of its function in MCS-48 sys­tems with external memory. It is provided continuous­ly on the ALE output pin.
## Reset
The reset input provides a means for initialization for the processor. This Schmitt-trigger input has an internal pull­up device which in combination with an external 1 µF capacitor provides an internal reset pulse of sufficient length to guarantee all circuitry is reset, as shown in 15. If the reset pulse is generated externally, the RESET pin must be held low for at least 10 milliseconds after the power supply is within tolerance. Only 5 machine cycles (6.8 µs @ 11 MHz) are required if power is already on and the oscillator has stabilized. ALE and PSEN (if EA = 1) are active while in Reset.
Reset performs the following functions:
1. Sets program counter to zero.
2. Sets stack pointer to zero.
3. Selects register bank 0.
4. Selects memory bank 0.
5. Sets BUS to high impedance state (except when EA = 5 V).
6. Sets Ports 1 and 2 to input mode.
7. Disables interrupts (timer and external).
8. Stops timer.
9. Clears timer flag.
10. Clears F0 and F1.
11. Disables clock output from T0.
## Single-Step
This feature, as pictured in 16, provides the user with a debug capability in that the processor can be stepped through the program one instruction at a time. While stopped, the address of the next instruction to be fetched is available concurrently on BUS and the lower half of Port 2. The user can therefore follow the program through each of the instruction steps. A timing diagram, showing the interaction between output ALE and input SS', is shown. The BUS buffer contents are lost during single step; however, a latch may be added to reestablish the lost I/O capability if needed. Data is valid at the leading edge of ALE.
#### TIMING
The 8048AH operates in a single-step mode as follows:
1. The processor is requested to stop by applying a low level on SS'.
2. The processor responds by stopping during the ad­dress fetch portion of the next instruction. If a double cycle instruction is in progress when the single step command is received, both cycles will be completed before stopping.
3. The processor acknowledges it has entered the stopped state by raising ALE high. In this state (which can be maintained indefinitely) the address of the next instruction to be fetched is present on BUS and the lower half of port 2.
4. SS' is then raised high to bring the processor out of the stopped mode allowing it to fetch the next instruction. The exit from stop is indicated by the processor brining ALE low.
5. To stop the processor at the next instruction, SS' must be brought low again soon after ALE goes low. If SS' is left high the processor remains in a "Run" mode.
A diagram for implementing the single-step function of the 8748Ah is show in 16. D-type flip-flop with preset and clear is used to generate SS'. In the run mode SS' is held high by keeping the flip-flop preset (preset has precedence over the clear input). To enter single step, preset is removed allowing ALE to bring SS' low via the clear input. ALE should be buffered since the clear input of an SN7474 is the equivalent of 3 TTL loads. The processor is now in the stopped state. The next instruction is initiated by clocking a "1" into the flip-flop. This "1" will not appear on SS' unless ALE is high removing clear from the flip-flop. In response to SS' going high the processor begins an instruction fetch which brings ALE low resetting SS' through the clear input and causing the processor to again enter the stopped state.
## Power Down Mode (8048AH, 8049AH, 8050AH, 8039AHL, 8035AHL, 8040AHL)
Extra circuitry has been added to the 8048AH/8049AH/ 8050AH ROM version to allow power to be removed from all but the data RAM array for low power standby oper­ation. In the power down mode the contents of data RAM can be maintained while drawing typically 10% to 15% of normal operating power requirements.
VCC serves as the 5V supply pin for the bulk of circuitry while the VDD pin supplies only the RAM array. In normal operation both pins are at 5V while in standby, VCC is at ground and VDD is maintained at its standard value. Ap­plying Reset to the processor through the RESET' pin inhibits any access to the RAM by the processor and guarantees the RAM cannot be inadvertently altered as power is removed from VCC.
A typical power down sequence (17) occurs as follows:
1. Imminent power supply failure is detected by user de­fined circuitry. Signal must be early enough to allow 8048AH to save all necessary data before VCC falls below normal operating limits.
2. Power fail signal is used to interrupt processor and vector it to a power fail service routine.
3. Power fail routine saves all important data and machine status in the internal data RAM array. Routine may also initiate transfer of backup supply to the VDD pin and indicate to external circuitry that power fail routine is complete.
4. Reset is applied to guarantee data will not be altered as the power supply falls out of limits. Reset must be held low until VCC is at ground level.
Recovery from the Power Down mode can occur as any other power-on sequence with an external capacitor on the Reset input providing the necessary delay. See the previous section on Reset.
## External Access Mode
Figure 16. Single Step Operation
Normally, the first 1K (8048AH), 2K (8049AH) or 4K (8050AH) words of program memory are automatically fetched from internal ROM or EPROM. The EA input pin however allows the user to efficiently disable internal program memory by forcing all program memory fetches to reference external memory. The following chapter ex­plains how access to external program memory is accomplished.
The External Access mode is very useful in system test and debug because it allows the user to disable his internal applications program and substitute an external program of his choice --- a diagnostic routine for instance. In addition, the data sheet shows how internal program memory can be read externally, independent of the processor. A "1" level on EA initiates the external access mode. For proper operation, Reset should be applied while the EA input is changed.
## Sync Mode
The 8048AH, 8049AH, 8050AH has incorporated a new SYNC mode. The Sync mode is provided to ease the design of multiple controller circuits by allowing the de­signer to force the device into known phase and state time. The SYNC mode may also be utilized by automatic test equipment (ATE) for quick, easy and efficient synchro­nizing between the tester and the DUT (device under test).
SYNC mode is enabled when SS' pin is raised to high voltage level of +12 volts. To begin synchronization, T0 is raised to 5 volts at least four clock cycles after SS'. T0 must be high for at least four X1 clock cycles to fully reset the prescaler and time state generators. T0 may then be brought down with the rising edge of X1. Two clock cycles later, with the rising edge of X1, the device enters into Time State 1, Phase 1. SS' is then brought down to 5 volts 4 clocks later after T0. RESET' is allowed to go high 5 tCY (75 clocks) later for normal execution of code. See 18.
# PIN DESCRIPTION
Figure 18. Sync Mode Timing
The MCS-48 processors are packaged in 40 pin Dual In-Line Packages (DIP's). 3 is a summary of the functions of each pin. 19 is the logic symbol for the 8048AH product family. Where it exists, the sec­ond paragraph describes each pin's function in an ex­panded MCS-48 system. Unless otherwise specified, each input is TTL compatible and each output will drive one standard TTL load.

Table 3. Pin Description
Designation	Pin Number*	Function
VSS	20	Circuit GND potential
VDD	26	Programming power supply; 21V during program for the 8748H/8749H; +5V during operation for both ROM and EPROM. Low power standby pin in 8048AH and 8049AH/8050AH ROM versions.
VCC	40	Main power supply; +5V during operation and during 8748H and 8749H programming.
PROG	25	Program pulse; +18V input pin during 8748H/8749H programming. Output strobe for 8243 I/O expander.
P10-P17 (Port 1)	27-34	8-bit quasi-bidirectional port. (Internal Pullup ≈ 50 kΩ)
P20-27 (Port 2)	21-24 35-38	8-bit quasi-bidirectional port. (Internal Pullup ≈ 50 kΩ) / P20-23 contain the four high order program counter bits during an external program mem­ory fetch and serve as a 4-bit O/O expander bus for 8243.
D0-D7 (BUS)	12-19	True bidirectional port which can be written or read synchronously using the RD', WR' strobes. The port can also be statically latched. / Contains the 8 low order program counter bits during an external program memory fetch, and receives the addressed instruction under the control of PSEN'. Also contains the address and data during an external RAM data store instruction, under control of ALE, RD' and WR'.
T0	1	Input pin testable using the conditional transfer instructions JT0 and JNT0. T0 can be des­ignated as a clock output using ENT0 CLK instruction. T0 is also used during programming and sync mode.
T1	39	Input pin testable using the JT1 and JNT1 instructions. Can be designated the event counter input using the STRT CNT instruction. (See Section 2.10).
INT'	6	Interrupt input. Initiates an interrupt if interrupt is enabled. Interrupt is disabled after a reset. (Active low) / Interrupt must remain low for at least 3 machine cycles to ensure proper operation.
RD'	8	Output strobe activated during a BUS read. Can be used to enable data onto the BUS from external device. (Active low)
RESET'	4	Input which is used to initialize the processor. Also used during EPROM programming and verification. (Active low) (Internal pullup ≈ 50 kΩ)
WR'	10	Output strobe during a BUS write. (Active low) Used as a write strobe to external data memory.
ALE	11	Address Latch Enable. This signal occurs once during each cycle and is useful as a clock output. / The negative edge of ALE strobes address into external data and program memory.
PSEN'	9	Program Store Enable. This output occurs only during a fetch to external program memory. (Active low)
SS'	5	Single step input can be used in conjunction with ALE to "single step" the processor through each instruction. (Active low) (Internal Pullup ≈ 300 kΩ) +12V for sync modes (See Section 2.16).

# PROGRAMMING, VERIFYING, AND ERASING EPROM
Table 3. Pin Description (Continued)
Designation	Pin Number*	Function
EA	7	External Access input which forces all program memory fetches to reference external memory. Useful for emulation and debug and essential for testing and program veri­fication. (Active high) +12V for 8048AH/8049AH/8050AH program verification and +18V for 8748H/8749H program verification (Internal Pullup ≈ 10 MΩ on 8048AH/8049AH/ 8035AHL/8039AHL/8050AH/8040AHL)
XTAL1	2	One side of crystal input for internal oscillator. Also input for external source.
XTAL2	3	Other side of crystal/external source input.

*Unless otherwise stated, inputs do not have internal pullup resistors. 8048AH, 8748H, 8049AH, 8050AH, 8040AHL
The internal Program Memory of the 8748H and the 8749H may be erased and reprogrammed by the user as explained in the following sections. See also the 8748H and 8749H data sheets.
## Programming/Verification
In brief, the programming process consists of: applying the program mode, applying an address, latching the ad­dress, applying data, and applying a programming pulse. This programming algorithm applies to both the 8748H and 8749H. Each word is programmed completely before moving on to the next and is followed by a verification step. The following is a list of the pins used for program­ming and a description of their functions:
Pin	Function
XTAL1	Clock Input (3 to 4.0 MHz)
Reset	Initialization and Address Latching
Test 0	Selection of Program (0 V) or Verify (5 V) Mode
EA	Activation of Program/Verify Modes
BUS	Address and Data Input. Data Output During Verify
P20-1	Address Input for 8748H
P20-2	Address Input for 8749H
VDD	Programming Power Supply
PROG	Program Pulse Input
P10-P11	Tied to ground (8749H only)

### 8748H and 8749H ERASURE CHARACTERISTICS
The erasure characteristics of the 8748H and 8749H are such that erasure begins to occur when exposed to light with wavelengths shorter than approximately 4000 Angs­troms (Å). It should be noted that the sunlight and certain types of fluorescent lamps have wavelengths in the 3000-4000 Å range. Data show that constant exposure to room level fluorescent lighting could erase the typical 8748H and 8749H in approximately 3 years while it would take approximately 1 week to cause erasure when exposed to direct sunlight. If the 8748H or 8749H is to be exposed to these types of lighting conditions for extended periods of time, opaque labels should be placed over the 8748H window to prevent unintentional erasure.
When erased, bits of the 8748H and 8749H Program Mem­ory are in the logic "0" state.
The recommended erasure procedure for the 8748H and 8749H is exposure to shortwave ultraviolet light which has a wavelength of 2537 Angstroms (Å). The integrated dose (i. e., UV intensity × exposure time) for erasure should be a minimum of 15 Wsec/cm2 power rating. The 8748H and 8749H should be placed within one inch from the lamp tubes during erasure. Some lamps have a filter in their tubes and this filter should be removed before erasure.

Figure 20. Program/Verify Sequence for 8749H/8748H

Table 4. A.C. Specification for Programming 8748H/8749H
Symbol	Parameter	Min	Max	Unit	Test Conditions
tAW	Address Setup Time to RESET' ↑	4tCY
tWA	Address Hold Time to RESET' ↑	4tCY
tDW	Data in Setup Time to PROG ↑	4tCY
tWD	Data in Hold Time after PROG ↓	4tCY
tPH	RESET' Hold Time to Verify	4tCY
tVDDW	VDD Hold Time before PROG ↑	0	1.0	ms
tVDDH	VDD Hold Time after PROG ↓	0	1.0	ms
tPW	Program Pulse Width	50	60	ms
tTW	TEST 0 Setup Time for Program Mode	4tCY
tWT	TEST 0 Hold Time after Program Mode	4tCY
tDO	TEST 0 to data Out Delay		4tCY
tWW	RESET' Pulse Width to Latch Address	4tCY
tr, tf	VDD and PROG Rise and Fall Times	0.5	100	µs
tCY	CPU Operation Cycle Time	3.75	5	µs
tRE	RESET' Setup Time before EA ↑	4tCY

TA = 25 °C; VCC = 5 V ±5%; VDD = 21 V ±5%
NOTE:
If TEST 0 is high, tDO can be triggered by RESET' ↑.

Figure 21. External Access Timing Waveforms

Figure 22. Port 1 / Port 2 Timing Waveforms

A.C. CHARACTERISTICS (TA = 0 °C to 70 °C; VCC = VDD = 5 V ± 10%; VSS = 0 V)
Symbol	Parameter		f (tCY) (Note 4)			11 MHz / Min Max			Unit	Conditions (Note 1)
tCY	Cycle Time		15/F(XTAL)			1.36		15.0	us	(Note 3)
tLL	ALE Pulse Width		7/30 tCY - 170			150			ns
tAL	Addr Setup to ALE		2/15 tCY - 110			70			ns	(Note 2)
tLA	Addr Hold from ALE		1/15 tCY - 40			50			ns
tCC1	Control Pulse Width (RD', WR')		1/2 tCY - 200			480			ns
tCC2	Control Pulse Width (PSEN')		2/5 tCY - 200			350			ns
tDW	Data Setup before WR'		13/30 tCY - 200			390			ns
tWD	Data Hold after WR'		1/15 tCY - 50			40			ns
tDR	Data Hold (RD', PSEN')		1/10 tCY - 30			0		110	ns
tRD1	RD' to Data In		11/30 tCY - 170					330	ns
tRD2	PSEN' to Data In		4/15 tCY - 170					190	ns
tAW	Addr Setup to WR'		1/3 tCY - 150			300			ns
tAD1	Addr Setup to Data (RD')		7/10 tCY - 220					730	ns
tAD2	Addr Setup to Data (PSEN')		1/2 tCY - 220					460	ns
tAFC1	Addr Float to RD', WR'		2/15 tCY - 40			140			ns	(Note 2)
tAFC2	Addr Float to PSEN'		1/30 tCY - 40			10			ns	(Note 2)
tLAFC1	ALE to Control (RD', WR')		1/5 tCY - 75			200			ns
tLAFC2	ALE to Control (PSEN')		1/10 tCY - 75			60			ns
tCA1	Control to ALE (RD', WR', PROG')		1/15 tCY - 40			50			ns
tCA2	Control to ALE (PSEN')		4/15 tCY - 40			320			ns
tCP	Port Control Setup to PROG'		2/15 tCY - 80			100			ns
tPC	Port Control Hold to PROG'		4/15 tCY - 200			160			ns
tPR	PROG' to P2 Input Valid		17/30 tCY - 120					650	ns
tPF	Input Data Hold from PROG'		1/10 tCY			0		140	ns
tDP	Output Data Setup		2/5 tCY - 150			400			ns
tPD	Output Data Hold		1/10 tCY - 50			90			ns
tPP	PROG' Pulse Width		7/10 tCY - 250			700			ns
tPL	Port 2 I/O Setup to ALE		4/15 tCY - 200			160			ns
tLP	Port 2 I/O Hold to ALE		1/30 tCY - 30			15			ns
tPV	Port Output from ALE		3/10 tCY + 100					510	ns
t0PRR	T0 Rep Rate		3/15 tCY			270			ns
Notes:
1. Control output CL = 80 pF BUS Outputs CL = 150 pF		2. BUS High Impedance Load 20 pF		3. f(tCY) assumes 50% duty cycle on X1 and X2.

			Instruction Code					Flags
Mnemonic	Function	Description	D7	D6	D5	D4	D3	D2	D1	D0	Cycles	Bytes	C	AC	F0	F1
Input/Output
ANL BUS, = data	(BUS) ← (BUS) AND data	Logical and immediate specified data with contents on BUS.	1 d7	0 d6	0 d5	1 d4	1 d3	0 d2	0 d1	0 d0	2	2
ANL Pp, = data	(Pp) ← (Pp) AND data p = 1 – 2	Logical and immediate specified data with designated port (1 – 2).	1 d7	0 d6	0 d5	1 d4	1 d3	0 d2	p d1	p d0	2	2
ANLD Pp, A	(Pp) ← (Pp) AND (A 0 – 3) p = 4 – 7	Logical and contents of Accumulator with designated port (4 – 7).	1	0	0	1	1	1	p	p	2	1
IN A, Pp	(A) ← (Pp); p = 1 – 2	Input data from designated port (1 – 2) into Accumulator.	0	0	0	0	1	0	p	p	2	1
INS A, BUS	(A) ← (BUS)	Input strobed BUS data into Accumulator.	0	0	0	0	1	0	0	0	2	1
MOVD A ,Pp	(A 0 – 3) ← (Pp); p = 4 – 7 (A 4 – 7) ← 0	Move contents of designated port (4 – 7) into Accumulator.	0	0	0	0	1	1	p	p	2	1
MOVD Pp, A	(Pp) ← A (0 – 3); p = 4 – 7	Move contents of Accumulator to designated port (4 – 7).	0	0	1	1	1	1	p	p	2	1
ORL BUS, = data	(BUS) ← (BUS) OR data	Logical or immediate specified data with contents of BUS.	1 d7	0 d6	0 d5	0 d4	1 d3	0 d2	0 d1	0 d0	2	2
ORLD Pp, A	(Pp) ← (Pp) OR (A 0 – 3) p = 4 – 7	Logical or contents of Accumulator with designated port (4 – 7).	1	0	0	0	1	1	p	p	2	1
ORL Pp, = data	(Pp) ← (Pp) OR data p = 1 – 2	Logical or immediate specified data with designated port (1 – 2).	1 d7	0 d6	0 d5	0 d4	1 d3	0 d2	p d1	p d0	2	2
OUTL BUS, A ⑤	(BUS) ← A	Output contents of Accumulator onto BUS.	0	0	0	0	0	0	1	0	2	1
OUTL Pp, A	(Pp) ← (A); p = 1 – 2	Output contents of Accumulator to designated port (1 – 2).	0	0	1	1	1	0	p	p	2	1
Registers
DEC Rr	(Rr) ← (Rr) – 1; r = 0 – 7	Decrement by 1 contents of designated register.	1	1	0	0	1	r	r	r	1	1
INC Rr	(Rr) ← (Rr) + 1; r = 0 – 7	Increment by 1 contents of designated register.	0	0	0	1	1	r	r	r	1	1
INC @ Rr	((Rr)) ← ((Rr)) + 1; r = 0 – 1	Increment indirect by 1 the contents of data memory location.	0	0	0	1	0	0	0	r	1	1
Subroutine
CALL addr	((SP)) ← (PC), (PSW 4 – 7) (SP) ← (SP) + 1 (PC 8 – 10) ← addr 8 – 10 (PC 0 – 7) ← addr 0 – 7 (PC 11) ← DBF	Call designated Subroutine.	a10 a7	a9 a6	a8 a5	1 a4	0 a3	1 a2	0 a1	0 a0	2	2
RET	(SP) ← (SP) – 1 (PC) ← ((SP))	Return from Subroutine without restoring Program Status Word.	1	0	0	0	0	0	1	1	2	1
RETR	(SP) ← (SP) – 1 (PC) ← ((SP)) (PSW 4 – 7) ← ((SP))	Return from Subroutine restoring Program Status Word.	1	0	0	1	0	0	1	1	2	1
Timer/Counter
EN TCNTI		Enable internal interrupt Flag for Timer/Counter output.	0	0	1	0	0	1	0	1	1	1
DIS TCNTI		Disable internal interrupt Flag for Timer Counter output.	0	0	1	1	0	1	0	1	1	1
MOV A, T	(A) ← (T)	Move contents of Timer/Counter into Accumulator.	0	1	0	0	0	0	1	0	1	1
MOV T, A	(T) ← (A)	Move contents of Accumulator into Timer/Counter.	0	1	1	0	0	0	1	0	1	1
STOP TCNT		Stop Count for Event Counter.	0	1	1	0	0	1	0	1	1	1
STRT CNT		Start Count for Event Counter.	0	1	0	0	0	1	0	1	1	1
STRT T		Start Count for Timer.	0	1	0	1	0	1	0	1	1	1

			Instruction Code					Flags
Mnemonic	Function	Description	D7	D6	D5	D4	D3	D2	D1	D0	Cycles	Bytes	C	AC	F0	F1
Miscellaneous
NOP		No Operation performed.	0	0	0	0	0	0	0	0	1	1
Accumulator
ADD A, = data	(A) ← (A) + data	Add immediate the specified Data to the Accumulator.	0 d7	0 d6	0 d5	0 d4	0 d3	0 d2	1 d1	1 d0	2	2	•	•
ADD A, Rr	(A) ← (A) + (Rr) r = 0 – 7	Add contents of designated register to the Accumulator.	0	1	1	0	1	r	r	r	1	1	•	•
ADD A, @ Rr	(A) ← (A) + ((Rr)) r = 0 – 1	Add indirect the contents of the data memory location to the Accumulator.	0	1	1	0	0	0	0	r	1	1	•	•
ADDC A, = data	(A) ← (A) + (C) + data	Add immediate with carry the specified data to the Accumulator.	0 d7	0 d6	0 d5	1 d4	0 d3	0 d2	1 d1	1 d0	2	2	•	•
ADDC A, Rr	(A) ← (A) + (C) + (Rr) r = 0 – 7	Add with carry the contents of the designated register to the Accumulator.	0	1	1	1	1	r	r	r	1	1	•	•
ADDC A, @ Rr	(A) ← (A) + (C) + ((Rr)) r = 0 – 1	Add indirect with carry the contents of data memory location to the Accumulator.	0	1	1	1	0	0	0	r	1	1	•	•
ANL A, = data	(A) ← (A) AND data	Logical and specified immediate data with Accumulator.	0 d7	1 d6	0 d5	1 d4	0 d3	0 d2	1 d1	1 d0	2	2
ANL A, Rr	(A) ← (A) AND (Rr) r = 0 – 7	Logical and contents of designated register with Accumulator.	0	1	0	1	1	r	r	r	1	1
ANL A, @ Rr	(A) ← (A) AND ((Rr)) r = 0 – 1	Logical and indirect the contents of data memory with Accumulator.	0	1	0	1	0	0	0	r	1	1
CPL A	(A) ← NOT (A)	Complement the contents of the Accumulator.	0	0	1	1	0	1	1	1	1	1
CLR A	(A) ← 0	CLEAR the contents of the Accumulator.	0	0	1	0	0	1	1	1	1	1
DA A		DECIMAL ADJUST the contents of the Accumulator.	0	1	0	1	0	1	1	1	1	1	•
DEC A	(A) ← (A) – 1	Decrement by 1 the Accumulator's contents.	0	0	0	0	0	1	1	1	1	1
INC A	(A) ← (A) + 1	Increment by 1 the Accumulator's contents.	0	0	0	1	0	1	1	1	1	1
ORL A, = data	(A) ← (A) OR data	Logical or specified immediate data with Accumulator.	0 d7	1 d6	0 d5	0 d4	0 d3	0 d2	1 d1	1 d0	2	2
ORL A, Rr	(A) ← (A) OR (Rr) r = 0 – 7	Logical or contents of designated register with Accumulator.	0	1	0	0	1	r	r	r	1	1
ORL A, @ Rr	(A) ← (A) OR ((Rr)) r = 0 – 1	Logical or indirect the contents of data memory with Accumulator.	0	1	0	0	0	0	0	r	1	1
RL A	(AN + 1) ← (AN); N = 0 – 6 (A0) ← (A7)	Rotate Accumulator left by 1-bit without carry.	1	1	1	0	0	1	1	1	1	1
RLC A	(AN + 1) ← (AN); N = 0 – 6 (A0) ← (C) (C) ← (A7)	Rotate Accumulator left by 1-bit through carry.	1	1	1	1	0	1	1	1	1	1	•
RR A	(AN) ← (AN + 1); N = 0 – 6 (A7) ← (A0)	Rotate Accumulator right by 1-bit without carry.	0	1	1	1	0	1	1	1	1	1
RRC A	(AN ) ← (AN + 1); N = 0 – 6 (A7) ← (C) (C) ← (A0)	Rotate Accumulator right by 1-bit through carry.	0	1	1	0	0	1	1	1	1	1	•
SWAP A	(A4 – 7) ⇄ (A0 – 3)	Swap the 2 4-bit nibbles in the Accumulator.	0	1	0	0	0	1	1	1	1	1
XRL A, = data	(A) ← (A) XOR data	Logical xor specified immediate data with Accumulator.	1 d7	1 d6	0 d5	1 d4	0 d3	0 d2	1 d1	1 d0	2	2
XRL A, Rr	(A) ← (A) XOR (Rr) r = 0 – 7	Logical xor contents of designated register with Accumulator.	1	1	0	1	1	r	r	r	1	1
XRL A, @ Rr	(A) ← (A) XOR ((Rr)) r = 0 – 1	Logical xor indirect the contents of data memory with Accumulator.	1	1	0	1	0	0	0	r	1	1

			Instruction Code					Flags
Mnemonic	Function	Description	D7	D6	D5	D4	D3	D2	D1	D0	Cycles	Bytes	C	AC	F0	F1
Branch
DJNZ Rr, addr	(Rr) ← (Rr) – 1; r = 0 – 7 if (Rr) ≠ 0: (PcC0 – 7) ← addr	Decrement the specified register and test contents.	1 a7	1 a6	1 a5	0 a4	1 a3	r a2	r a1	r a0	2	2
JBb addr	(PC 0 – 7) ← addr if Bb = 1 (PC) ← (PC) + 2 if Bb = 0	Jump to specified address if Accumulator bit is set.	b2 a7	b1 a6	b0 a5	1 a4	0 a3	0 a2	1 a1	0 a0	2	2
JC addr	(PC 0 – 7) ← addr if C = 1 (PC) ← (PC) + 2 if C = 0	Jump to specified address if carry flag is set.	1 a7	1 a6	1 a5	1 a4	0 a3	1 a2	1 a1	0 a0	2	2
JF0 addr	(PC 0 – 7) ← addr if F0 = 1 (PC) ← (PC) + 2 if F0 = 0	Jump to specified address if Flag F0 is set.	1 a7	0 a6	1 a5	1 a4	0 a3	1 a2	1 a1	0 a0	2	2
JF1 addr	(PC 0 – 7) ← addr if F01= 1 (PC) ← (PC) + 2 if F1 = 0	Jump to specified address if Flag F1 is set.	0 a7	1 a6	1 a5	1 a4	0 a3	1 a2	1 a1	0 a0	2	2
JMP addr	(PC 8 – 10) ← addr 8 – 10 (PC 0 -7) ← add 0 – 7 (PC 11) ← DBF	Direct Jump to specified address within the 2K address block.	a10 a7	a9 a6	a8 a5	0 a4	0 a3	1 a2	0 a1	0 a0	2	2
JMPP @ A	(PC 0 – 7) ← ((A))	Jump indirect to specified address within address page.	1	0	1	1	0	0	1	1	2	1
JNC addr	(PC 0 – 7) ← addr if C = 0 (PC) ← (PC) if C = 1	Jump to specified address if carry flag is low.	1 a7	1 a6	1 a5	0 a4	0 a3	1 a2	1 a1	0 a0	2	2
JNI addr	(PC 0 – 7) ← addr if I = 0 (PC) ← (PC) if I = 1	Jump to specified address if interrupt is low.	1 a7	0 a6	0 a5	0 a4	0 a3	1 a2	1 a1	0 a0	2	2
JNT0 addr	(PC 0 – 7) ← addr if T0 = 0 (PC) ← (PC) if T0 = 1	Jump to specified address if Test 0 is low.	0 a7	0 a6	1 a5	0 a4	0 a3	1 a2	1 a1	0 a0	2	2
JNT1 addr	(PC 0 – 7) ← addr if T1 = 0 (PC) ← (PC) if T1 = 1	Jump to specified address if Test 1 is low.	0 a7	1 a6	0 a5	0 a4	0 a3	1 a2	1 a1	0 a0	2	2
JNZ addr	(PC 0 – 7) ← addr if A ≠ 0 (PC) ← (PC) if A = 0	Jump to specified address if Accumulator is non-zero.	1 a7	0 a6	0 a5	1 a4	0 a3	1 a2	1 a1	0 a0	2	2
JTF addr	(PC 0 – 7) ← addr if TF = 1 (PC) ← (PC) if TF = 0	Jump to specified address if Timer Flag is set to 1.	0 a7	0 a6	0 a5	1 a4	0 a3	1 a2	1 a1	0 a0	2	2
JT0 addr	(PC 0 – 7) ← addr if T0 = 1 (PC) ← (PC) if T0 = 0	Jump to specified address if Test 0 is a 1.	0 a7	0 a6	1 a5	1 a4	0 a3	1 a2	1 a1	0 a0	2	2
JT1 addr	(PC 0 – 7) ← addr if T1 = 1 (PC) ← (PC) if T1 = 0	Jump to specified address if Test 1 is a 1.	0 a7	1 a6	0 a5	1 a4	0 a3	1 a2	1 a1	0 a0	2	2
JZ addr	(PC 0 – 7) ← addr if A = 0 (PC) ← (PC) if A ≠ 0	Jump to specified address if Accumulator is 0.	1 a7	1 a6	0 a5	0 a4	0 a3	1 a2	1 a1	0 a0	2	2
Control
EN I		Enable the external Interrupt input.	0	0	0	0	0	1	0	1	1	1
DIS I		Disable the external Interrupt input.	0	0	0	1	0	1	0	1	1	1
ENT0 CLK		Enable the Clock Output pin T0.	0	1	1	1	0	1	0	1	1	1
SEL MB0	(DBF) ← 0	Select Bank 0 (locations 0 – 2047) of Program Memory.	1	1	1	0	0	1	0	1	1	1
SEL MB1	(DBF) ← 1	Select Bank 1 (locations 2048 – 4095) of Program Memory.	1	1	1	1	0	1	0	1	1	1
SEL RB0	(BS) ← 0	Select Bank 0 (locations 0 – 7) of Data Memory.	1	1	0	0	0	1	0	1	1	1
SEL RB1	(BS) ← 1	Select Bank 1 (locations 24 – 31) of Data Memory.	1	1	0	1	0	1	0	1	1	1

Notes:	① Instruction Code Designators r and p form the binary representation of the Registers and Ports involved.
② The dot under the appropriate flag bit indicates that its content is subject to change by the instruction it appears in.
③ References to the address and data are specified in bytes 2 and or 1 of the instruction.
④ Numerical Subscritions appearing in the FUNCTION column reference the specific bits affected.
⑤ When the Bus is written to with an OUTL instruction, the Bus remains an Output Port until either device is reset or a MOVX instruction is executed.

# INSTRUCTION SET
The MCS-48 instruction set is extensive for a machine of its size and has been tailored to be straightforward and very efficient in its use of program memory. All instructions are either one or two bytes in length and over 70% are only one byte long. Also, all instructions execute in either one or two cycles (2.5 µsec or 5.0 µsec when using a 6 MHz XTAL) and over 50% of all instructions execute in a single cycle. Double cycle instructions include all immediate instructions and all I/O instructions.
The MCS-48 microcomputers have been designed to efficiently handle arithmetic operations in both binary and BCD as well as to efficiently handle the single bit operations required in control applications. Special instructions have also been included to simplify loop counters, table lookup routines, and N-way branch routines.
#### Data Transfers
The 8-bit accumulator is the central point for all data transfers within the 8048. Data can be transferred between the 8 registers of each working register bank and the accumulator directly, i.e. The source or destination register is specified by the instruction. The remaining locations of the internal RAM array are referred to as Data Memory and are addressed indirectly via an address stored in either R0 or R1 of the active working register bank. R0 and R1 are also used to indirectly address external data memory when it is present. Transfers to and from internal RAM require one cycle while transfers to external RAM require two. Constants stored in Program Memory can be loaded directly to the accumulator and to the 8 working registers. Data can also be transferred directly between the on-board timer/counter or the accumulator and the Program Status Word (PSW). Writing to the PSW alters machine status accordingly and provides a means of restoring status after an interrupt or of altering the stack pointer if necessary.
#### Accumulator Operations
Immediate data, data memory or the working registers can be added with or without carry to the accumulator. These sources can also be ANDed, ORed or Exclusive ORed to the accumulator. Data may be moved to or from the accumulator and working registers or data memory. The two values can also be exchanged in a single operation.
In addition, the lower 4 bits of the accumulator can be exchanged with the lower 4 bits of any of the internal RAM locations. This instruction, along with an instruction which swaps the upper and lower 4-bit halves of the accu­mulator, provides easy handling of 4-bit quantities, including BCD numbers. To facilitate BCD arithmetic, a Decimal Adjust instruction is included. This instruction is used to correct the result of the binary addition of two two-digit BCD numbers. Performing a decimal adjust on the result in the accumulator produces the required BCD result.
Finally, the accumulator can be: incremented, de­cre­mented, cleared or complemented and can be rotated left or right 1 bit at a time with or without carry.
Although there is no subtract instruction in the 8048, this operation can be easily implemented with three single-byte single-cycle instructions.
A value may be subtracted from the accumulator with the result in the accumulator by:
Complement Accumulator	CPL A
Add register to Accumulator	ADD A, Rr
Complement Accumulator	CPL A

#### Register Operations
The working registers can be accessed via the accu­mulator as explained above or can be loaded immediate with constraints from program memory. In addition, they can be incremented or decremented or used as loop counters using the decrement and skip, if not zero instruction, as explained under branch instructions.
All Data Memory including working registers can be accessed with indirect instructions via R0 and R1 and can be incremented.
#### Flags
There are four user accessible flags in the 8048: Carry, Auxiliary Carry, F0, and F1. Carry indicates overflow of the accumulator and Auxiliary Carry is used to indicate overflow between BCD digits and is used during decimal adjust operation. Both Carry and Auxiliary Carry are accessible as part of the Program Status word and are stored on the stack during subroutines. F0 and F1 are undedicated general purpose flags to be used as the programmer desires. Both flags can be cleared or comple­mented and tested by conditional jump instructions. F0 is also accessible via the Program Status word and is stored on the stack with the carry flags.
#### Branch Instructions
The unconditional jump instruction is two bytes and allows jumps anywhere in the first 2K words of program memory. Jumps to the second 2K of memory (4K words are directly addressable) are made by first executing a select memory bank instruction then executing the jump instruction. The 2K boundary can only be crossed via a jump or subroutine call instruction, i.e. The bank switch does not occur until a jump is executed. Once a memory bank has been selected all subsequent jumps will be to the selected bank until another select memory bank instruction is executed. A subroutine in the opposite bank can be accessed by a select memory bank instruction followed by a call instruction. Upon completion of the subroutine execution will automatically return to the original bank; however, unless the original bank is reselected, the next jump instruction encountered will again transfer execution to the opposite bank.
Conditional jumps can test the following inputs and machine status:
T0 Input pin
T1 Input pin
INT' Input pin
Accumulator Zero
Any bit of Accumulator
Carry Flag
F0 Flag
F1 Flag
Conditional jumps allow a branch to any address within the current page (256 words) of execution. The conditions tested are the instantaneous values at the time the conditional jump is executed. For instance, the jump on accumulator zero instruction tests the accumulator itself not an intermediate zero flag.
The decrement register and skip if not zero instruction combines a decrement and a branch instruction to create an instruction very useful in implementing a loop counter. This instruction can designate any one of the 8 working registers as a counter and can effect a branch to any address within the current page of execution.
A single byte indirect jump instruction allows the program to be vectored to any one of several locations based on the contents of the accumulator. The contents of the accumulator points to a location in program memory which contains the jump address. The 8-bit jump address refers to the current page of execution. This instruction could be useful, for instance, to vector to any one of several routines based on an ASCII character which has been loaded in the accumulator. In this way ASCII key inputs can be used to initiate various routines.
#### Subroutines
Subroutines are entered by executing a call instruction. Calls can be made like unconditional jumps to any address in a 2K word bank and jumps across the 2K boundary are executed in the same manner. Two separate return instructions determine whether or not status (upper 4 bits of PSW) is restored upon return from the subroutine.
The return and restore status instruction also signals the end of an interrupt service routine if one has been in progress.
#### Timer Instructions
The 8-bit on board timer/counter can be loaded or read via the accumulator while the counter is stopped or while counting. The counter can be started as a timer with an internal clock source or as an event counter or timer with an external clock applied to the T1 input pin. The instruction executed determines which clock source is used. A single instruction stops the counter whether it is operating with an internal or an external clock source. In addition, two instructions allow the timer interrupt to be enabled or disabled.
#### Control Instructions
Two instructions allow the external interrupt source to be enabled or disabled. Interrupts are initially disabled and are automatically disabled while an interrupt service routine is in progress and re-enabled afterwards.
There are four memory bank select instructions, two to designate the active working register bank and two to control program memory banks. The operation of the memory bank switch is explained in section 6.1.2. The working register bank switch instructions allow the programmer to immediately substitute a second 8 register working register bank for the one in use. This effectively provides 16 working registers or it can be used as a means of quickly saving the contents of the registers in response to an interrupt. The user has the option to switch or not to switch banks on interrupt. However, if the banks are switched, the original bank will be automatically restored upon execution of a return and restore status instruction at the end of the interrupt service routine.
A special instruction enables an internal clock, which is the XTAL frequency divided by three, to be output on pin T0. This clock can be used as a general purpose clock in the user system. This instruction should be used only to initialize the system since the clock output can be disabled only by application of system reset.
#### Input/Output Instructions
Ports 1 and 2 are 8-bit static I/O ports which can be loaded to and from the accumulator. Outputs are statically latched but inputs are not latched and must be read while inputs are present. In addition, immediate data from program memory can be ANDed or ORed directly to Port 1 and Port 2 with the result remaining on the port. This allows “masks” stored in program memory to selectively set or reset individual bits of the I/O ports. Ports 1 and 2 are configured to allow input an a given pin by first writing a “1” out to th pin.
An 8-bit port called BUS can also be accessed via the accumulator and can have statically latched outputs as well. It too can have immediate data ANDed or ORed directly to its outputs, however, unlike Ports 1 and 2, all eight lines of BUS must be treated as either input or output at any one time. In addition to being a static port, BUS can be used as a true synchronous bi-directional port using the Move External instructions used to access external data memory. When these instructions are executed a corresponding READ or WRITE pulse is generated and data is valid only at this time. When data is not being transferred BUS is in a high impedance state.
The basic three on board I/O ports can be expanded via a 4-bit expander bus using half of Port 2. I/O expander devices on this bus consist of four 4-bit ports which are addressed as ports 4 through 7. These ports have their own AND and OR instructions like the on board ports as well as move instructions to transfer data in and out. The expander AND and OR instructions, however, combine the contents of accumulator with the selected port rather than immediate data as is done with the on board ports.
I/O devices can also be added externally using the BUS port as the expansion bus. In this case the I/O ports become “memory mapped”, i.e. They are addressed in the same way as external data memory and exist in the external data memory address space addressed by pointer register R0 or R1.
## Instruction Set Description
The following pages describe the MCS-48 instruction set in detail. The instruction set is first summarized with instructions grouped functionally. This summary page is followed by a detailed description listed alphabetically by mnemonic opcode.
The alphabetic listing includes the following information:
Mnemonic
Machine Code
Verbal Description
Symbolic Description
The machine code is represented with the most significant bit (7) to the left and two byte instructions are represented with the first byte on the left.

ADD A, Rr					Add Register Contents to Accumulator
	(A) ← (A) + (Rr)								r = 0 – 7
	The contents of register Rr is added to the Accumulator. The Carry flag is modified according to the result of the operation.
	0	1	1	0	1	r	r	r

ADD A, @ Rr					Add Data Memory Contents to Accumulator
	(A) ← (A) + ((Rr))								r = 0 – 1
	The contents of the Data Memory location addressed by bits 0 – 5 (0 – 6 for 8039/8049) of register Rr is added to the Accumulator. The Carry flag is modified according to the result of the operation.
	0	1	1	0	0	0	0	r

ADD A, data					Add Immediate Data to Accumulator
	(A) ← (A) + data									2 cycles
	The contents byte that follows the opcode is added to the Accumulator. The Carry flag is modified according to the result of the operation.
	0	0	0	0	0	0	1	1
	d7	d6	d5	d4	d3	d2	d1	d0

ADDC A, Rr					Add Carry and Register Contents to Accumulator
	(A) ← (A) + (C) + (Rr)								r = 0 – 7
	The Carry flag is added to the Accumulator and then cleared. Afterwards, the contents of register Rr is added to the Accumulator. The Carry flag is modified according to the result of the operation.
	0	1	1	1	1	r	r	r

ADDC A, @ Rr					Add Carry and Data Memory Contents to Accumulator
	(A) ← (A) + (C) + ((Rr))								r = 0 – 1
	The Carry flag is added to the Accumulator and then cleared. Afterwards, the contents of the Data Memory location addressed by bits 0 – 5 (0 – 6 for 8039/8049) of register Rr is added to the Accumulator. The Carry flag is modified according to the result of the operation.
	0	1	1	1	0	0	0	r

ADDC A, data					Add Carry and Immediate Data to Accumulator
	(A) ← (A) + (C) + data									2 cycles
	The Carry flag is added to the Accumulator and then cleared. Afterwards, the contents byte that follows the opcode is added to the Accumulator. The Carry flag is modified according to the result of the operation.
	0	0	0	1	0	0	1	1
	d7	d6	d5	d4	d3	d2	d1	d0

ANL A, Rr					Logical AND Accumulator with Register Mask
	(A) ← (A) ∧ (Rr)								r = 0 – 7
	The contents of the Accumulator is logically (bitwise) anded with the contents of register Rr.
	0	1	0	1	1	r	r	r

ANL A, @ Rr					Logical AND Accumulator with Memory Mask
	(A) ← (A) ∧ ((Rr))								r = 0 – 1
	The contents of the Accumulator is logically (bitwise) anded with the contents of the Data Memory location addressed by bits 0 – 5 (0 – 6 for 8039/8049) of register Rr.
	0	1	0	1	0	0	0	r

ANL A, data					Logical AND Accumulator with Immediate Mask
	(A) ← (A) ∧ data									2 cycles
	The contents of the Accumulator is logically (bitwise) anded with the contents of the byte that follows the opcode.
	0	1	0	1	0	0	1	1
	d7	d6	d5	d4	d3	d2	d1	d0

ANL BUS, data					Logical AND BUS with Immediate Mask
	(BUS) ← (BUS) ∧ data									2 cycles
	BUS is read and its contents is logically (bitwise) anded with the contents of the byte that follows the opcode. This instruction requires the instruction OUTL BUS, A to be executed in advance. / Note: This instruction is not available for the 8021/8022. It must not be used with the 8035/8039 as BUS is used for external Program Memory access.
	1	0	0	1	1	0	0	0
	d7	d6	d5	d4	d3	d2	d1	d0

ANL Pp, data					Logical AND Port 1 – 2 with Immediate Mask
	(Pp) ← (Pp) ∧ data								p = 1 – 2	2 cycles
	Port p is read and its contents is logically (bitwise) anded with the contents of the byte that follows the opcode. / Note: This instruction is not available for the 8021/8022.
	1	0	0	1	1	0	p	p
	d7	d6	d5	d4	d3	d2	d1	d0

ANLD Pp, A					Logical AND Port 4 – 7 with Accumulator Mask
	(Pp) ← (Pp) ∧ A(0 – 3)								p = 4 – 7			2 cycles
	Port p is read and its bits 0 – 3 are logically (bitwise) anded with bits 0 - 3 of the Accumulator.
	1	0	0	1	1	1	p	p	p	1 – 0			Port
										0 0 1 1	0 1 0 1		4 5 6 7

CALL addr					Subroutine Call
	((SP)) ← (PC), (PSW 4 – 7) (SP) ← (SP) + 1 (PC 8 – 10) ← addr 8 – 10 (PC 0 – 7) ← addr 0 – 7 (PC 11) ← DBF									2 cycles
	The Program Counter and bits 4 to 7 of the PSW are stored on the Program Stack. The Program Stack Counter (PSW 0 – 2) is updated. Program execution continues at the Program Memory location addressed by addr. Bit 11 of the Program Counter is initialized with DBF (determined by last SEL MBx instruction). / A CALL instruction cannot begin at Program Memory locations 2046-2047 or 4094-4095. / The program execution resumes with the next instruction after the CALL.
	a10	a9	a8	1	0	1	0	0
	a7	a6	a5	a4	a3	a2	a1	a0

CLR A					Clear Accumulator
	(A) ← 0
	The contents of the Accumulator is cleared to 0.
	0	0	1	0	0	1	1	1

CLR C					Clear Carry Bit
	(C) ← 0
	The Carry bit is cleared to 0. / The Carry bit can set by ADD, ADDC, RL C, CPL C, RRC an DAA.
	1	0	0	1	0	1	1	1

CLR F0					Clear Flag 0
	(F0) ← 0
	Flag 0 is cleared to 0. / Note: This instruction is not available for the 8021/8022.
	1	0	0	0	0	1	0	1

CLR F1					Clear Flag 1
	(F1) ← 0
	Flag 1 is cleared to 0. / Note: This instruction is not available for the 8021/8022.
	1	0	1	0	0	1	0	1

CPL A					Complement Accumulator
	(A) ← ¬ (A)
	The contents of the Accumulator is inverted (one's complement).
	0	0	1	1	0	1	1	1

CPL C					Complement Carry Bit
	(C) ← ¬ (C)
	The contents of the Carry bit is inverted.
	1	0	1	0	0	1	1	1

CPL F0					Complement Flag 0
	(F0) ← ¬ (F0)
	The contents of the Flag 0 is inverted. / Note: This instruction is not available for the 8021/8022.
	1	0	0	1	0	1	0	1

CPL F1					Complement Flag 1
	(F1) ← ¬ (F1)
	The contents of the Flag 1 is inverted. / Note: This instruction is not available for the 8021/8022.
	1	0	1	1	0	1	0	1

DA A					Decimal Adjust Accumulator
	The 8-bit value in the Accumulator is modified resulting in two BCD-encoded values.
	1)	If the value of bits 0 – 3 is greater than 9 or AC is set then 6 is added to the contents of the Accumulator.
	2)	If the value of bits 4 – 7 is now greater than 9 or C is set then 6 is added to the most significant nibble.
	Example: The Accumulator contains 10011011.
	C 0 0 1		AC 0 0 0			7 1 1 0 0	0 0 1 0	0 1 1 0		4 1 0 0 0		3 1 0 0 0		0 1 0 0		1 1 0 0	0 1 0 1 1	Add 6 to bits 0 – 7 Add 6 to bits 4 – 7 Overflow to Carry
	0	1		0	1		0		1		1		1

DEC A					Decrement Accumulator
	(A) ← (A) – 1
	The contents of the Accumulator is decremented by 1.
	0	0	0	0	0	1	1	1

DEC Rr					Decrement Register
	(Rr) ← (Rr) – 1								r = 0 – 1
	The contents of register Rr is decremented by 1. / Note: This instruction is not available for the 8021/8022.
	1	1	0	0	1	r	r	r

DIS I					Disable External Interrupt
	Disable external interrupt requests. / Note: This instruction is not available for the 8021.
	0	0	0	1	0	1	0	1

DIS TCNTI					Disable Timer/Counter Interrupt
	Disable Timer/Counter interrupt request. A pending interrupt request is cleared. Overflow of the counter does not trigger an interrupt, although the counter continues its operation and sets the T flag eventually. / Note: This instruction is not available for the 8021.
	0	0	1	1	0	1	0	1

DJNZ Rr, addr					Decrement Register and Test
	(Rr) ← (Rr) – 1 (PC 0 – 7) ← addr; if Rr ≠ 0 (PC) ← (PC) + 2; if Rr = 0								r = 0 – 7	2 cycles
	The contents of register Rr is decremented by 1 and tested for zero. If all bits are 0 then program execution is continued with the next instruction. If not all bits are 0 then a jump to the given address is done. / The address must be an 8-bit value, i. e. the jump will be within the current page (256 bytes). If the DJNZ instruction is at location 255 of a page then the jump destination will be located in the following page.
	1	1	1	0	1	r	r	r
	a7	a6	a5	a4	a3	a2	a1	a0

EN I					Enable External Interrupt
	Enable external interrupt request. / Note: This instruction is not available for the 8021.
	0	0	0	0	0	1	0	1

EN TCNTI					Enable Timer/Counter Interrupt
	Enable Timer/Counter interrupts request. / Note: This instruction is not available for the 8021.
	0	0	1	0	0	1	0	1

ENT0 CLK					Enable Clock Output
	Enables the clock output at T0 pin. A reset deactivates this function. / Note: This instruction is not available for the 8021/8022.
	0	1	1	1	0	1	0	1

IN A, Pp					Input Port or Data to Accumulator
	(A) ← (Pp)								p = 1 – 2	2 cycles
	Port p is read and its contents is stored in the Accumulator. / For the 8021 the instruction IN A, P2 triggers storing of P 20 – 23 to the Accumulator bits 0 – 3 (bits 4 – 7 are cleared to 0).
	0	0	0	0	1	0	p	p

INC A					Increment Accumulator
	(A) ← (A) + 1
	The contents of the Accumulator is incremented by 1.
	0	0	0	1	0	1	1	1

INC Rr					Increment register
	(Rr) ← (Rr) + 1								r = 0 – 7
	The contents of register Rr is incremented by 1.
	0	0	0	1	1	r	r	r

INC @ Rr					Increment Data Memory Location
	((Rr)) ← ((Rr)) + 1								r = 0 – 1
	the contents of the Data Memory location addressed by bits 0 – 5 (0 – 6 for 8039/8049) of register Rr is incremented by 1.
	0	0	0	1	0	0	0	r

IN A, P0		Input of Port 0 Data to Accumulator
	Equivalent to INS A, BUS but not RD' strobe is generated. Note: This instruction is only available for the 8021/8022.

INS A, BUS					Strobed Input of BUS Data to Accumulator
	(A) ← (BUS)									2 cycles
	BUS is read with a low-strobe on RD' and it contents is transferred to the Accumulator. / Note: This instruction must not be used with the 8035/8039 as BUS is used for external Program Memory access.
	0	0	0	0	1	0	0	0

JBb addr					Jump if Accumulator Bit is Set
	(PC 0 – 7) ← addr; if Bb = 1 (PC) ← (PC) + 2; if Bb = 0								b = 0 – 7	2 cycles
	If Accumulator bit b is set then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is not set then program execution continues with the next instruction. / Note: This instruction is not available for the 8021/8022.
	b2	b1	b0	1	0	0	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JC addr					Jump if Carry is Set
	(PC 0 – 7) ← addr; if C = 1 (PC) ← (PC) + 2; if C = 0									2 cycles
	If Carry is set then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is not set then program execution continues with the next instruction.
	1	1	1	1	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JF0 addr					Jump if Flag 0 is Set
	(PC 0 – 7) ← addr; if F0 = 1 (PC) ← (PC) + 2; if F0 = 0									2 cycles
	If Flag 0 is set then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is not set then program execution continues with the next instruction. / Note: This instruction is not available for the 8021/8022.
	1	0	1	1	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JF1 addr					Jump if Flag 1 is Set
	(PC 0 – 7) ← addr; if F1 = 1 (PC) ← (PC) + 2; if F1 = 0									2 cycles
	If Flag 1 is set then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is not set then program execution continues with the next instruction. / Note: This instruction is not available for the 8021/8022.
	0	1	1	1	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JMP addr					Direct Jump
	(PC 8 – 10) ← addr 8 – 10 (PC 0 – 7) ← addr 0 – 7 (PC 11) ← DBF									2 cycles
	Program execution continues at the Program Memory location addressed by addr. Bit 11 of the Program Counter is initialized with DBF (determined by last SEL MBx instruction).
	a10	a9	a8	0	0	1	0	0
	a7	a6	a5	a4	a3	a2	a1	a0

JMPP @ A					Indirect Jump Within Page
	(PC 0 – 7) ← ((A))									2 cycles
	The contents of the Program Memory location addressed by the Accumulator is used as the new page offset of the Program Counter.
	1	0	1	1	0	0	1	1

JNC addr					Jump if Carry is Not Set
	(PC 0 – 7) ← addr; if C = 0 (PC) ← (PC) + 2; if C = 1									2 cycles
	If Carry is not set then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is set then program execution continues with the next instruction.
	1	1	1	0	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JNI addr					Jump if Interrupt Input is Low
	(PC 0 – 7) ← addr; if I = 0 (PC) ← (PC) + 2; if I = 1									2 cycles
	If the external interrupt input pin is low then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is high then program execution continues with the next instruction. / Note: This instruction is not available for the 8021/8022.
	1	0	0	0	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JNT0 addr					Jump if Test 0 is Low
	(PC 0 – 7) ← addr; if T0 = 0 (PC) ← (PC) + 2; if T0 = 1									2 cycles
	If Test 0 is low then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is high then program execution continues with the next instruction. / Note: This instruction is not available for the 8021/8022.
	0	0	1	0	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JNT1 addr					Jump if Test 1 is Low
	(PC 0 – 7) ← addr; if T1 = 0 (PC) ← (PC) + 2; if T1 = 1									2 cycles
	If Test 1 is low then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is high then program execution continues with the next instruction.
	0	1	0	0	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JNZ addr					Jump if Accumulator is Not Zero
	(PC 0 – 7) ← addr; if Accu ≠ 0 (PC) ← (PC) + 2; if Accu = 0									2 cycles
	If the Accumulator contents is not all zero then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is all zero then program execution continues with the next instruction.
	1	0	0	1	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JTF addr					Jump if Timer/Counter Flag is Set
	(PC 0 – 7) ← addr; if T = 1 (PC) ← (PC) + 2; if T = 0									2 cycles
	If the Timer/Counter flag is set then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is not set then program execution continues with the next instruction. / This instruction clears the Timer/Counter flag after it has been read.
	0	0	0	1	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JT0 addr					Jump if Test 0 is High
	(PC 0 – 7) ← addr; if T0 = 1 (PC) ← (PC) + 2; if T0 = 0									2 cycles
	If Test 0 is high then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is low then program execution continues with the next instruction. / Note: This instruction is not available for the 8021/8022.
	0	0	1	1	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JT1 addr					Jump if Test 1 is High
	(PC 0 – 7) ← addr; if T1 = 1 (PC) ← (PC) + 2; if T1 = 0									2 cycles
	If Test 1 is high then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is low then program execution continues with the next instruction.
	0	1	0	1	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

JZ addr					Jump if Accumulator is Zero
	(PC 0 – 7) ← addr; if Accu = 0 (PC) ← (PC) + 2; if Accu ≠ 0									2 cycles
	If the Accumulator contents is all zero then a jump is executed to the Program Memory location addressed by the byte that follows the opcode. If it is not all zero then program execution continues with the next instruction.
	1	1	0	0	0	1	1	0
	a7	a6	a5	a4	a3	a2	a1	a0

MOV A, data					Move Immediate Data to Accumulator
	(A) ← data									2 cycles
	The Accumulator is loaded with the contents of the Program Memory location that follows the opcode .
	0	0	1	0	0	0	1	1
	d7	d6	d5	d4	d3	d2	d1	d0

MOV A, PSW					Move PSW Contents to Accumulator
	(A) ← (PSW)
	The contents of the PSW is copied into the Accumulator. / Note: This instruction is not available for the 8021/8022.
	1	1	0	0	0	1	1	1

MOV A, Rr					Move Register Contents to Accumulator
	(A) ← (Rr)								r = 0 – 7
	The contents of register Rr is copied into the Accumulator.
	1	1	1	1	1	r	r	r

MOV A, @ Rr					Move Data Memory Contents to Accumulator
	(A) ← ((Rr))								r = 0 – 1
	The contents of the Data Memory location addressed by bits 0 – 5 (0 – 6 for the 8039/8049) is copied into the Accumulator.
	1	1	1	1	0	0	0	r

MOV A, T					Move Timer/Counter Contents to Accumulator
	(A) ← (T)
	The contents of the Timer/Counter register is copied into the Accumulator.
	0	1	0	0	0	0	1	0

MOV PSW, A					Move Accumulator Contents to PSW
	(PSW) ← (A)
	The contents of the Accumulator is copied into the PSW (all bits). / Note: This instruction is not available for the 8021/8022.
	1	1	0	1	0	1	1	1

MOV Rr, A					Move Accumulator Contents to Register
	(Rr) ← (A)								r = 0 – 7
	The contents of the Accumulator is copied into register Rr.
	1	0	1	0	1	r	r	r

MOV Rr, data					Move Immediate Data into Register
	(Rr) ← data								r = 0 – 7	2 cycles
	The contents of the Program Memory location that follows the opcode is copied into register Rr.
	1	0	1	1	1	r	r	r
	d7	d6	d5	d4	d3	d2	d1	d0

MOV @ Rr, A					Move Accumulator Contents to Data Memory
	((Rr)) ← (A)								r = 0 – 1
	The contents of the Accumulator is copied into the Data Memory location addressed by bits 0 – 5 (0 – 6 for the 8039/8049).
	1	0	1	0	0	0	0	r

MOV @ Rr, data					Move Immediate Data to Data Memory
	((Rr)) ← data								r = 0 – 1	2 cycles
	The byte that follows the opcode is copied into the Data Memory location addressed by bits 0 – 5 (0 – 6 for 8039/8049) of register Rr.
	1	0	1	1	0	0	0	r
	d7	d6	d5	d4	d3	d2	d1	d0

MOV T, A					Move Accumulator Contents to Timer/Counter
	(T) ← (A)
	The contents of the Accumulator is copied into the Timer/Counter register.
	0	1	1	0	0	0	1	0

MOVD A, Pp					Move Port 4 – 7 Data to Accumulator
	(A 0 – 3) ← (Pp) (A 4 – 7) ← 0								p = 4 – 7	2 cycles
	Port p is read and its bits 0 – 3 are copied into the Accumulator. Bits 4 – 7 of the Accumulator are cleared to 0. / See the ANLD Pp, A instruction for coding of the p field.
	0	0	0	0	1	1	p	p

MOVD Pp, A					Move Accumulator Data to Port 4 – 7
	(Pp) ← (A 0 – 3)								p = 4 – 7	2 cycles
	Bits 0 – 3 of the Accumulator are copied to port p. / See the ANLD Pp, A instruction for coding of the p field.
	0	0	1	1	1	1	p	p

MOVP A, @ A					Move Current Page Data to Accumulator
	(PC 0 – 7) ← (A) (A) ← ((PC))									2 cycles
	The contents of the Program Memory location addressed by the Accumulator is copied into the Accumulator. Only bits 0 – 7 of the Program Counter are affected. Therefore, the instruction is restricted to the current page. The Program Counter is restored after the operation. / Note: If the instruction is located at address 255 of the current page then the next page is addressed with the Accumulator as offset.
	1	0	1	0	0	0	1	1

MOVP3 A, @ A					Move Page 3 Data to Accumulator
	(PC 0 – 7) ← (A) (PC 8 – 11) ← 0011 (A) ← ((PC))									2 cycles
	The contents of the Program Memory location addressed by the Accumulator in page 3 is copied into the Accumulator. The Program Counter is restored after the operation.
	1	1	1	0	0	0	1	1

MOVX A, @ Rr					Move External Data Memory Contents to Accumulator
	(A) ← ((Rr))								r = 0 – 1	2 cycles
	The contents of the external Data Memory location addressed by register Rr is copied into the Accumulator. / Note: This instruction is not available for the 8021/8022.
	1	0	0	0	0	0	0	r

MOVX @ Rr, A					Move Accumulator Contents to External Data Memory
	((Rr)) ← (A)								r = 0 – 1	2 cycles
	The contents of the Accumulator is copied to the external Data Memory location addressed by register Rr. / Note: This instruction is not available for the 8021/8022.
	1	0	0	1	0	0	0	r

NOP					No Operation
	No operation is executed. Program execution continues with the next instruction.
	0	0	0	0	0	0	0	0

ORL A, Rr					Logical OR Accumulator With Register Mask
	(A) ← (A) ∨ (Rr)								r = 0 – 7
	The contents of the Accumulator is logically (bitwise) ored with the contents of register Rr.
	0	1	0	0	1	r	r	r

ORL A, @ Rr					Logical OR Accumulator With Memory Mask
	(A) ← (A) ∨ ((Rr))								r = 0 – 1
	The contents of the Accumulator is logically (bitwise) ored with the contents of the Data Memory location addressed by bits 0 – 5 (0 – 6 for the 8039/8049).
	0	1	0	0	0	0	0	r

ORL A, data					Logical OR Accumulator With Immediate Mask
	(A) ← (A) ∨ data									2 cycles
	The contents of the Accumulator is logically (bitwise) ored with the contents of the Program Memory location following the opcode.
	0	1	0	0	0	0	1	1
	d7	d6	d5	d4	d3	d2	d1	d0

ORL BUS, data					Logical OR BUS with Immediate Mask
	(BUS) ← (BUS) ∨ data									2 cycles
	BUS is read and its contents is logically (bitwise) ored with the contents of the byte that follows the opcode. This instruction requires the instruction OUTL BUS, A to be executed in advance. / Note: This instruction is not available for the 8021/8022. It must not be used with the 8035/8039 as BUS is used for external Program Memory access.
	1	0	0	0	1	0	0	0
	d7	d6	d5	d4	d3	d2	d1	d0

ORL Pp, data					Logical OR Port 1 – 2 With Immediate Mask
	(Pp) ← (Pp) ∨ data								p = 1 – 2	2 cycles
	Port p is read and its contents is logically (bitwise) ored with the contents of the byte that follows the opcode. / Note: This instruction is not available for the 8021/8022.
	1	0	0	0	1	0	p	p
	d7	d6	d5	d4	d3	d2	d1	d0

ORLD Pp, A					Logical OR Port 4 – 7 With Accumulator Mask
	(Pp) ← (Pp) ∨ A(0 – 3)								p = 4 – 7	2 cycles
	Port p is read and its bits 0 – 3 are logically (bitwise) ored with bits 0 - 3 of the Accumulator. / See the ANLD Pp, A instruction for coding of the p field. / Note: This instruction is not available for the 8021/8022.
	1	0	0	0	1	1	p	p

OUTL P0, A					Output Accumulator Data to Port 0
	Note: This instruction is only available for the 8021/8022.
	1	0	0	1	0	0	0	0

OUTL BUS, A					Output Accumulator Data to BUS
	(BUS) ← (A)									2 cycles
	The contents of the Accumulator is put on the BUS with a low-strobe on WR'. The BUS lines maintain their contents until the next OUTL BUS, A instruction. All other instructions related to BUS (except INS A, BUS) destroy the BUS state. This also includes the MOVX instructions. Note: This instruction is not available for the 8021/8022.
	0	0	0	0	0	0	1	0

OUTL Pp, A					Output Accumulator Data to Port 1 – 2
	(Pp) ← (A)								p = 1 – 2	2 cycles
	The contents of the Accumulator is put on port p. The port lines maintain their contents until they are modified by another instruction related to port Pp.
	0	0	1	1	1	0	p	p

RAD					Move Conversion Result Register to Accumulator
										2 cycles
	The contents of the A/D result register is copied into the Accumulator. / Note: This instruction is only available for the 8022.
	1	0	0	0	0	0	0	0

RET					Return Without PSW Restore
	(SP) ← (SP) – 1 (PC) ← ((SP))									2 cycles
	The Program Stack Counter is decremented by 1. Using this new address, the Program Counter is restored from the Program Stack. / Bits 4 – 7 of the PSW are not restored.
	1	0	0	0	0	0	1	1

RETI					Return from Interrupt
	(SP) ← (SP) – 1 (PC) ← ((SP)) + 1									2 cycles
	The Program Stack Counter is decremented by 1. Using this new address, the Program Counter is restored from the Program Stack. / The interrupt logic enables a new interrupt request. / Note: This instruction is only available for the 8022.
	1	0	0	1	0	0	1	1

RETR					Return With PSW Restore
	(SP) ← (SP) – 1 (PC) ← ((SP)) (PSW 4 – 7) ← ((SP))									2 cycles
	The Program Stack Counter is decremented by 1. Using this new address, the Program Counter is restored from the Program Stack. In addition, bits 4 – 7 of the PSW are restored from the Program Stack. / This instruction should only be used to return from an interrupt service subroutine. Moreover, it should not be used for call/returns within the interrupt service routine as it clears the interrupt flag and thus enables a new interrupt request to be processed by the system (interrupt nesting). / Note: This instruction is not available for the 8021/8022.
	1	0	0	1	0	0	1	1

RL A					Rotate Left Without Carry
	(A n+1) ← (A n); n = 0 – 6 (A 0) ← (A 7)
	The contents of the Accumulator is rotated left by one bit position.
	1	1	1	0	0	1	1	1

RLC A					Rotate Left With Carry
	(A n+1) ← (A n); n = 0 – 6 (A 0) ← (C) (C) ← (A 7)
	The contents of the Accumulator is rotated left through Carry by one bit position.
	1	1	1	1	0	1	1	1

RR A					Rotate Right Without Carry
	(A n) ← (A n+1); n = 0 – 6 (A 7) ← (A 0)
	The contents of the Accumulator is rotated right by one bit position.
	0	1	1	1	0	1	1	1

RRC A					Rotate Right With Carry
	(A n) ← (A n+1); n = 0 – 6 (A 7) ← (C) (C) ← (A 0)
	The contents of the Accumulator is rotated right through Carry by one bit position.
	0	1	1	0	0	1	1	1

SEL AN0					Select Analog Input 0
	Input 0 of the A/D converter is selected and a new conversion is started. A running conversion is aborted and restarted. / Note: This instruction is only available for the 8022.
	1	0	0	1	0	1	0	1

SEL AN1					Select Analog Input 1
	Input 1 of the A/D converter is selected and a new conversion is started. A running conversion is aborted and restarted. / Note: This instruction is only available for the 8022.
	1	0	0	0	0	1	0	1

SEL MB0					Select Memory Bank 0
	(DBF) ← 0
	MBF is set to 0, selecting bank 0 of the Program Memory. The following JMP and CALL instructions will target the locations 0 – 2047 of the Program Memory. / Note: This instruction is not available for the 8021/8022.
	1	1	1	0	0	1	0	1

SEL MB1					Select Memory Bank 1
	(DBF) ← 1
	MBF is set to 1, selecting bank 1 of the Program Memory. The following JMP and CALL instructions will target the locations 2048 – 4095 of the Program Memory. / Note: This instruction is not available for the 8021/8022.
	1	1	1	1	0	1	0	1

SEL RB0					Select Register Bank 0
	(BS) ← 0
	Bit 4 of PSW is set to 0. Registers 0 – 7 are mapped to Data Memory locations 0 – 7. This is the recommended setting for normal program execution. / Note: This instruction is not available for the 8021/8022.
	1	1	0	0	0	1	0	1

SEL RB1					Select Register Bank 1
	(BS) ← 1
	Bit 4 of PSW is set to 1. Register s0 – 7 are mapped to Data Memory locations 24 – 31. / This is the recommended setting for interrupt service subroutines as Data Memory locations 0 – 7 are not modified. The RETR instruction at the end of the interrupt subroutine will restore BS (bit 4 of PSW). / Note: This instruction is not available for the 8021/8022.
	1	1	0	1	0	1	0	1

STOP TCNT					Stop Timer/Counter
	The Timer/Counter is stopped.
	0	1	1	0	0	1	0	1

STRT CNT					Start Event Counter
	T1 is declared as input for the Event Counter. Every high-to-low transition at T1 increments the counter register by 1.
	0	1	0	0	0	1	0	1

STRT T					Start Timer
	The internal clock is declared as input for the Timer Counter. After 32 machine cycles, the counter register is incremented by 1. This instruction resets the prescaler to 0 by does not change the counter register.
	0	1	0	1	0	1	0	1

SWAP A					Swap Nibbles Within Accumulator
	(A 4 – 7) ⇄ (A 0 – 3)
	Bits 0 – 3 and 4 – 7 of the Accumulator are swapped.
	0	1	0	0	0	1	1	1

XCH A, Rr					Exchange Accumulator and Register Contents
	(A) ⇄ (Rr)								r = 0 – 7
	The contents of the Accumulator is exchanged with the contents of register Rr.
	0	0	1	0	1	r	r	r

XCH A, @ Rr					Exchange Accumulator and Data Memory Contents
	(A) ⇄ ((Rr))								r = 0 – 1
	The contents of the Accumulator is exchanged with the contents of the Data Memory location addressed by bits 0 – 5 (0 – 6 for the 8039/8049).
	0	0	1	0	0	0	0	r

XCHD A, @ Rr					Exchange Accumulator and Data Memory 4-Bit Data
	(A 0 – 3) ⇄ ((Rr))								r = 0 – 1
	The bits 0 – 3 of the Accumulator are exchanged with bits 0 – 3 of the Data Memory location addressed by bits 0 – 5 (0 – 6 for the 8039/8049).
	0	0	1	1	0	0	0	r

XRL A, Rr					Logical XOR Accumulator With Register Mask
	(A) ← (A) ⊕ (Rr)								r = 0 – 7
	The contents of the Accumulator is logically (bitwise) xored with the contents of register Rr.
	1	1	0	1	1	r	r	r

XRL A, @ Rr					Logical XOR Accumulator With Memory Mask
	(A) ← (A) ⊕ ((Rr))								r = 0 – 1
	The contents of the Accumulator is logically (bitwise) xored with the contents of the Data Memory location addressed by bits 0 – 5 (0 – 6 for the 8039/8049).
	1	1	0	1	0	0	0	r

XRL A, data					Logical XOR Accumulator With Immediate Mask
	(A) ← (A) ⊕ data									2 cycles
	The contents of the Accumulator is logically (bitwise) xored with the contents of the Program Memory location following the opcode.
	1	1	0	1	0	0	1	1
	d7	d6	d5	d4	d3	d2	d1	d0

# Summary
If the capabilities resident on the single-chip 8048/8049, 8748 or 8045/8039 are not sufficient for your system requirements, special on-board circuitry allows the addition of a wide variety external memory, I/O or special peripherals you may require. The processor can be directly and simply expanded in the following areas:
- Program Memory to 4K words
- Data Memory to 320 words (384 words with 8049)
- I/O by unlimited amount
- Special Functions using 8080/8085 peripherals
By using bank switching techniques maximum capability is essentially unlimited. Bank switching is discussed later in the chapter. Expansion is accomplished in two ways:
1. Expander I/O --- A special I/O Expander circuit the 8243 provides for the addition of four 4-bit Input/Output ports with the sacrifice of only the lower half (4 bits) of port 2 for inter-device communication. Multiple 8243s may be added to this 4-bit bus by generating the required “chip select” lines.
2. Standard 8085 Bus --- One port of the 8048 is like the 8 bit bidirectional data bus of the 8085 microcomputer system allowing interface to the numerous standard memories and peripherals of the MCS-80/85 micro­computer family.
MCS-48 systems can be configured using either both of these expansion features to optimize system capabilities to the application. Both expander devices and standard memories and peripherals can be added virtually any number and combination required.
## Expansion of Program Memory
Program Memory is expanded beyond the resident 1K or 2K words by using the 8058 BUS feature of the MCS-48. All program memory fetches from addresses less than 1024 (2048) occur internally with no external signals being generated (except ALE which is always present). At address 1024 the 8048 automatically initiates external program memory fetches.
### Instruction Fetch Cycle (External)
For all instruction fetches from addresses of 1024 (2048) or greater the following will occur:
1. The contents of the 12 bit program counter will be output on BUS and the lower half of port 2.
2. Address Latch Enable (ALE) will indicate the time at which address is valid. The trailing edge of ALE is used to latch the address externally.
3. Program Store Enable (PSEN') indicates that an external instruction fetch is in progress and serves to enable the external memory device.
4. BUS reverts to input (floating) mode and the processor accepts its 8 bit contents as an instruction word.
All instruction fetches including internal addresses can be forced to be external by activating the EA pin of the 8048/8049. The 8035/8039 processors without program memory always operate in the external program memory mode (EA = 5 V).
### Extended Program Memory Addressing (Beyond 2K)
For programs of 2K words or less, the 8048/8049 addres­ses program memory in the conventional manner. Addresses beyond 2047 can be reached by executing a program memory bank switch instruction (SEL MB0, SEL MB1) followed by a branch instruction (JMP or CALL). The bank switch feature extends the range of branch instructions beyond their normal 2K range and at the same time prevents the user from inadvertently crossing the 2K boundary.
#### Program Memory Bank Switch
The switching of 2K program memory banks is accomplished by directly setting or resetting the most significant bit of the program counter (bit 11). Bit 11 is not altered by normal incrementing of the program counter but is loaded with the contents of a special flip-flop each time a JMP or CALL instruction is executed. This special flip-flop is set by executing an SEL MB1 and reset by SEL MB0. Therefore, the SEL MB instruction may be executed at any time prior to the actual bank switch which occurs during the next branch instruction encountered. Since all twelve bits of the program counter including bit (11) are stored in the stack when a CALL is executed, the user may jump to subroutines across the 2K boundary and the proper bank will be restored upon return. However, the bank switch flip-flop will not be altered on return.
#### Interrupt Routines
Interrupts always vector the program counter to location 3 or 7 in the first 2K bank and bit 11 of the program counter is held at “0” during the interrupt service routine. The end of the service routine is signaled by the execution of an RETR instruction. Interrupt service routines should therefore be contained entirely in the lower 2K words of program memory. The execution of a SEL MB0 or SEL MB1 instruction within an interrupt routine is not recommended since it will not alter PC11 while in the routine, but will change the internal flip-flop.
### Restoring I/O Port Information
Although the lower half of Port 2 is used to output the four most significant bits of address during an external program memory fetch, the I/O information is still output during certain portions of each machine cycle. I/O information is always present on Port 2 lower at the rising edge of ALE and can be sampled or latched at this time.
## Expansion of Data Memory
Data Memory is expanded beyond the resident 64 words by using the 8085 type bus feature of the MCS-48.
### Read/Write Cycles
All address and data is transferred over the 8 lines of BUS. A read or write cycle occurs as follows:
1. The contents of register R0 or R1 is outputted on BUS.
2. Address Latch Enable (ALE) indicates address is valid. The trailing edge of ALE is used to latch the address externally.
3. A read (RD') or write (WR') pulse on the corresponding output pins of the 8048 indicates the type of data memory access in progress. Output data is valid at the trailing edge of WR' and input data must be valid at the trailing edge of RD'.
4. Data (8-bits) is transferred in or out over BUS.
### Addressing External Data Memory
External Data Memory is accessed with its own two-cycle move instructions MOVX A, @R and MOVX @R, A which transfer 8 bits of data between the accumulator and the external memory location addressed by the contents of one of the RAM Pointer Registers R0 or R1. This allows 256 locations to be addressed in addition to the resident locations. Additional pages may be added by “bank switching” with extra output lines of the 8048.
## Expansion of Input/Output
There are four possible modes of I/O expansion with the 8048: one using a special low cost expander, the 8243; another using standard MCS-80/85 I/O devices; and a third using the combination memory/I/O expander devices the 8155, 8355 and 8755. It is also possible to expand using standard TTL devices.
### I/O Expander Device
The most efficient means of I/O expansion for small systems is the 8243 I/O Expander Device which requires only 4 port lines (lower half of Port 2) for communication with the 8048. The 8243 contains four 4-bit I/O ports which serve as extension of the on chip I/O and are addressed as ports #4 – 7. The following operations may be performed on these ports:
1. Transfer Accumulator to Port.
2. Transfer Port to Accumulator.
3. AND Accumulator to Port.
4. OR Accumulator to Port.
A 4-bit transfer from a port to the lower half of the Accu­mulator sets the most significant four bits to zero. All communication between the 8048 and the 8243 occurs over Port 2 lower (P20 – P23) with timing provided by an output pulse on the PROG pin of the processor. Each transfer consists of two 4-bit nibbles:
The first containing the “op code” and port address and the second containing the actual 4 bits of data.
Nibble 1					Nibble 2
3	2	1	0		3	2	1	0
I	I	A	A		d	d	d	d

Instruction Code			Port Address
II			AA
00	Read		00	--	Port	#4
01	Write		01	--	Port	#5
10	OR		10	--	Port	#5
11	AND		11	--	Port	#6

A high to low transition of the PROG line indicates that address is present while a low to high transition indicates the presence of data. Additional 8243s may be added to the four bit bus and chip selected using additional output lines from the 8048/8748.
#### I/O Port Characteristics
Each of the four 4-bit ports of the 8243 can serve as either input or output and can provide high drive capability in both the high and low state.
### I/O Expansion with Standard Peripherals
Standard MCS-80/85 type I/O devices may be added to the MCS-48 using the same bus and timing used for Data Memory expansion. I/O devices reside on the Data Memory bus and in the data memory address space and are accessed with the same MOVX instructions. See the previous section on data memory expansion for a description of timing. The following are a few of the Standard MCS-80 devices which are very useful in MCS-48 systems.
8214	Priority Interrupt Encoder
8251	Serial Communications Interface
8255	General Purpose Programmable I/O
8279	Keyboard/Display Interface
8253	Interval Timer

### Combination Memory and I/O Expanders
As mentioned in the sections on program and data memory expansion the 8355/8755 and 8155 expanders also contain I/O capability.
8355/8755: These two parts are ROM and EPROM equivalents and therefore contain the same I/O structure. I/O consists of two 8-bit ports which normally reside in the external data memory address space and are accessed with MOVX instructions. Associated with each port is an 8-bit Data Direction Register which defines each bit in the port as either an input or an output. The data direction registers are directly addressable thereby allowing the user to define under software control each individual bit of the ports as either input or output. All outputs are statically latched and double buffered. Inputs are not latched.
8155/8156: I/O on the 8155/8156 is configured as two 8-bit programmable I/O ports and one 6-bit programmable port. These three registers and a Control/Status register are accessible as external data memory with the MOVX instructions. The contents of the control register deter­mines the mode of the three ports. The ports can be programmed as input or output with or without associated handshake communication lines. In the handshake mode, lines of the six-bit port become input and output strobes for the two 8-bit ports. See the data sheet below for details. Also included in the 8155 is a 14-bit programmable timer. The clock input to the timer and the timer overflow output are available on external pins. The timer can be programmed to stop on terminal count or to continuously reload itself. A square wave or pulse output on terminal count can also be specified.
## Memory Bank Switching
Certain systems may require more than the 4K words of program memory which are directly addressable by the program counter or more than the 256 data memory and I/O locations directly addressable by the pointer registers R0 and R1. These systems can be achieved using “bank switching” techniques. Bank switching is merely the sel­ection of various blocks or “banks” of memory using dedicated output port lines from the processor. In the case of the 8048 program memory is selected in blocks of 4K words at a time while data memory and I/O are enabled 256 words at a time.
The most important consideration in implementing two or more banks is the software required to cross the bank boundaries. Each crossing of the boundary requires that the processor first write a control bit to an output port before accessing memory or I/O in the new bank. If program memory is being switched, programs should be organized to keep boundary crossing to a minimum. Jumping to subroutines across the boundary should be avoided when possible since the programmer must keep track of which bank to return to after completion of the subroutine. If these subroutines are to be nested and accessed from either bank, a software “stack” should be implemented to save the bank switch bit just as if were another bit of the program counter.
From a hardware standpoint bank switching is very straight-forward and involves only the connection of an I/O line or lines as bank enable signals. These enables are ANDed with normal memory and I/O chip select signals to activate the proper bank.
## Control Signal Summary
The following table summarizes the instructions which activate the various control outputs of the MCS-48 pro­cessor.
CONTROL SIGNAL	WHEN ACTIVE
RD'	DURING MOVX A, @R OR INS BUS
WR'	DURING MOVX @R, A OR OUTL BUS
ALE	EVERY MACHINE CYCLE
PSEN'	DURING FETCH OF EXTERNAL PROGRAM MEMORY (INSTRUCTION OR IMMEDIATE DATA)
PROG	DURING	MOVD A, P ANLD P, A MOVD P, A ORLD P, A

During all other instructions these outputs are driven to the inactive state.
## Port Characteristics
#### BUS Port Operations
The BUS port can operate in three different modes: as a latched I/O port, as a bi-directional bus port, or as a pro­gram memory address output when external memory is used. The BUS port lines are either active high, active low or high impedance (floating). The latched mode (INS, OUTL) is intended for use in the single chip configuration where BUS is not being used as an expander port. OUTL and MOVX instructions can be mixed if necessary. However, a previously latched output will be destroyed by executing a MOVX instruction and BUS will be left in the high impedance state. OUTL should never be used in a system with external program memory, since latching BUS can cause the next instruction, if external, to be fetched improperly.
#### Port 2 Operations
The lower half of Port 2 can be used in three different ways: as a quasi, bi-directional static port, as an 8243 expander port and to address external program memory. In all cases outputs are driven low by an active device and driven high momentarily by an active device and held high by a 50 KΩ resistor to +5 V.
The port may contain latched I/O data prior to its use in another mode without affecting operation of either. If lower Port 2 (P20-3) is used to output address for an external program memory fetch the I/O information previously latched will be automatically removed temporarily while address is present then restored when the fetch is complete. However, if lower Port 2 is used to communi­cate with an 8243, previously latched I/O information will be removed and not restored. After an input from the 8243 P(20-3) will be left in the input mode (floating). After an output to the 8243 P(20-3) will contain the value written, ANDed or ORed to the 8243 port.

8243
MCS-48® INPUT/OUTPUT EXPANDER

• Low Cost	• 24-Pin DIP
• Simple Interface to MCS-48® Microcomputers	• Single 5V Supply
	• High Output Drive
• Four 4-Bit I/O Ports	• Direct Extension of Resident 8048 I/O Ports
• AND and OR Directly to Ports

The Intel® 8243 is an input/output expander designed specifically to provide a low cost means of I/O expansion for the MCS-48 family of single chip microcomputers. Fabricated in 5 volts NMOS, the 8243 combines low cost, single supply voltage and high drive capability.
The 8243 consists of four 4-bit bidirectional static I/O ports and one 4-bit port which serves as an interface to the MCS-48 microcomputers. The 4-bit interface requires that only 4 I/O lines of the 8048 be used for I/O expansion, and also allows multiple 8243's to be added to the same bus.
The I/O ports of the 8243 serve as a direct extension of the resident I/O facilities of the MCS-48 microcomputers and are accessed by their own MOV, ANL and ORL instructions.

Figure 24. 8243 Pin Configuration
Figure 23. 8243 Block Diagram
Table 6. Pin Description
Symbol	Pin No.	Function
PROG	7	CLOCK INPUT. A high to low transition on PROG signifies that address and control are available on P20 – P23, and a low to high transition signifies that data is available on P20 – P23.
CS'	6	CHIP SELECT INPUT. A high on CS inhibits any change of output or internal status.
P20 – P23	11 – 8	Four (4) bit bi-directional port contains the address and control bits on a high to low transition of PROG. During a low to high transition, contains the data for a selected output port if a write operation, or the data from a selected port before the low to high transition if a read operation.
GND	12	0 volt supply.
P40 – P43 P50 – P53 P60 – P63 P70 – P73	2 – 5 1,23 – 21 20 – 17 13 – 16	Four (4) bit bi-directional I/O ports. May be programmed to be input (during read), low impedance latched output (after write), or a tristate (after read). Data on pins P20 – P23 may be directly written, ANDed or ORed with previous data.
VCC	24	+5 volt supply.

FUNCTIONAL DESCRIPTION
General Operation
The 8243 contains four 4-bit I/O ports which serve as an extension of the on-chip I/O and are addressed as ports 4 – 7. The following operations may be performed on these ports:
- Transfer Accumulator to Port
- Transfer Port to Accumulator
- AND Accumulator to Port
- OR Accumulator to Port
All communication between the 8048 and the 8243 occurs over Port 2 (P20 – P23) with timing provided by an output pulse on the PROG pin of the processor. Each transfer consists of two 4-bit nibbles.
The first containing the “op code” and port address and the second containing the actual 4-bits of data. A high to low transition of the PROG line indicates that address is present while a low to high transition indicates the presence of data. Additional 8243's may be added to the 4-bit bus and chip selected using additional output lines from the 8048/8748/8035.
Power On Initialization
Initial application of power to the device forces input/ output ports 4, 5, 6, and 7 to the tri-state and port 2 to the input mode. The PROG pin may be either high or low when power is applied. The first high to low transition of PROG causes device to exit power on mode. The power on sequence is initiated if VCC drops below 1V.
		Address			Instruction
P21	P20	Code	P23	P22	Code
0	0	Port 4	0	0	Read
0	1	Port 5	0	1	Write
1	0	Port 6	1	0	ORLD
1	1	Port 7	1	1	ANLD

Write Modes
The device has three write modes. MOVD Pi, A directly writes new data into the selected port and old data is lost. ORLD Pi, A takes new data, OR's it with the old data and then writes it to the port. ANLD Pi, A takes new data, AND's it with the old data and then writes it to the port. Operation code and port address are latched from the input port 2 on the high to low transition of the PROG pin. On the low to high transition of PROG, data on port 2 is transferred to the logic block of the specified output port.
After the logic manipulation is performed, the data is latched and output. The old data remains latched until new valid outputs are entered.
Read Mode
The device has one read mode. The operation code and port address are latched from the input port 2 on the high to low transition of the PROG pin. As soon as the read operation and port address are decoded, the appropriate outputs are tri-stated and the input buffers switched on. The read operation is terminated by a low to high transition of the PROG pin. The port (4, 5, 6 or 7) that was selected is switched to the tri-state mode while port 2 is returned to the input mode.
Normally, a port will be in an output (write mode) or input (read mode). If modes are changed during operation, the first read following a write should be ignored; all following reads are valid. This is to allow the external driver on the port to settle after the first read instruction removes the low impedance drive from the 8243 output. A read of any port will leave that port in a high impedance state.
ASOLUTE MAXIMUM RATINGS*
Ambient Temperature Under Bias	0 °C to 70 °C
Storage Temperature	-65 °C to +150 °C
Voltage on Any Pin
With Respect to Ground	-0.5 V to +7 V
Power Dissipation	1 W

D.C. CHARACTERISTICS TA = 0 °C to 70 °C, VCC = 5 V ±10%
Symbol	Parameter	Min	Typ	Max	Units	Test Conditions
VIL	Input Low Voltage	-0.5		0,8	V
VIH	Input High Voltage	0,2		VCC + 0.5	V
VOL1	Output Low Voltage Ports 4 – 7			0,45	V	IOL = 4.5 mA*
VOL2	Output Low Voltage Port 7			1	V	IOL = 20 mA
VOH1	Output High Voltage Ports 4 – 7	2,4			V	IOH = 240 µA
IL1	Input Leakage Ports 4 – 7	-10		20	µA	VIN = VCC to 0 V
IL2	Input Leakage Port 2, CS, PROG	-10		10	µA
VOL3	Output Low Voltage Port 2			0,45	V	IOL = 0.6 mA
ICC	VCC Supply Current		10	20	mA
VOL2	Output Voltage Port 2	2,4			V	IOH = 100 µA
IOL	Sum of all IOL from 16 Outputs			72	mA	4.5 mA Each Pin

* See following graph for additional sink current capability.
A.C. CHARACTERISTICS TA = 0 °C to 70 °C, VCC = 5 V ±10%
Symbol	Parameter	Min	Max	Units	Test Conditions
tA	Code Valid Before PROG	100		ns	80 pF Load
tB	Code Valid After PROG	60		ns	20 pF Load
tC	Data Valid Before PROG	200		ns	80 pF Load
tD	Data Valid After PROG	20		ns	20 pF Load
tH	Floating After PROG	0	150	ns	20 pF Load
tK	PROG Negative Pulse Width	700		ns
tCS	CS Valid Before / After PROG	50		ns
tPO	Ports 4 – 7 Valid After PROG		700	ns	100 pF Load
tLP1	Ports 4 – 7 Valid Before / After PROG	100		ns
tACC	Port 2 Valid After PROG		650	ns	80 pF Load

* Notice: Stresses above those listed under “Absolute Maximum Ratings” may cause permanent damage to the device. This is a stress rating only and functional opera­tion of the device at these or any other conditions above those indicated in the operational sections of this specification is not implied. Exposure to absolute maximum rating conditions for extended periods affect device reliability.

WAVEFORMS

Sink Capability
Figure 25.
The 8243 can sink 5 mA @ 0.45 V on each of its 16 I/O lines simultaneously. If, however, all lines are not sinking simultaneously or all lines are not fully loaded, the drive capability of any individual line increases as is shown by the accompanying curve.
For example, if only 5 of the 16 lines are to sink current at one time, the curve shows that each of those 5 lines is capable of sinking 9 mA @ 0.45 V (if any lines are to sink 9 mA the total IOL must not exceed 45 mA or five 9 mA loads).
Example: How many pins can drive 5 TTL loads (1.6 mA) assuming remaining pins are unloaded?
IOL = 5 x 1.6 mA = 8 mA
∈IOL = 60 mA from curve
# pins = 60 mA ÷ 8 mA/pin = 7.5 = 7
In this case, 7 lines can sink can sink 8 mA for a total of 56 mA. This leaves 4 mA sink current capability which can be divided in any way among the remaining 8 i/O lines of the 8243.
Example: This example shows how the use of the 20 mA sink capability of Port 7 affects the sinking capability of the other I/O lines.
An 8243 will drive the following loads simultaneously.
2 loads – 20 mA @ 1 V (port 7 only)
8 loads – 4 mA @ 0.45 V
6 loads – 3.2 mA @ 0.45 V
is this within the specified limits?
∈IOL = (2 x 20) + (8 x 4) + (6 x 3.2) = 91.2 mA. From the curve: for IOL = 4 mA, ∈IOL ≈ 93 mA. Since 91.2 mA < 93 mA the loads are within the specified limits.
Although the 20 mA @ 1 V loads are used in calculating ∈IOL, it is the largest current required @ 0.45 V which determines the maximum allowable ∈IOL.
NOTE:
A 10 kΩ to 50 kΩ pullup resistor to +5 V should be added to 8243 outputs when driving to 5 V CMOS directly.

Figure 26. Expander Interface

Figure 27. Output Expander Timing
Figure 28. Using Multiple 8243's

The 8245 is a general purpose graphics display device that operates in conjunction with raster scan type displays. Its primary purpose is to provide a means for generating and moving objects on a TV screen for use in the customer game market. However, its generality and flexibility makes it suitable for use also in teaching machines, animation displays, simulation trainers, and etc.

This device is a peripheral that communicates over the data and address bus of the 8048/8748. Although other microprocessors may be used with it, these particular devices provide the greatest capability for the low system cost.

FEATURES

. Single 5V supply
. 28 pin CerDip or plastic DIP package.
. 8048/8748/8085 Compatible.
. Partial color TV sync generator, CCIR standards.
. Provides shapes that are mask programmable in internal ROM.
. Accommodate up to 32 object locations on the display simultaneously.
. Devices may be multiplexed to provide greater than 32 object locations on the
   display.
. All movement of objects displayed is under software control in the microprocessor.
. Display objects that collide return status and location information to the micro-
   processor.
. Provides Red, Green, Blue, Luminance, and Sound outputs.

* Note: Signals that are asserted when the variable is low voltage are designated by
        a overline {~~} , eg. overline CS is active low.

SYMBOL I/O

D0-D7 I/O Data/Address lines to/from 8048/8749.
overline CS I Chip Select enables writing to or reading from the addressed
        Functional block within the device.
ALE I Address Latch Enable allows the contents of the multiplexed address/
        data bus to be interpreted as an address.
overline WR I Write Strobe causes the bus data to be written into the previously
        selected memory element.
overline RD I Read Strobe allows status and counter information to be read from
        the device.
overline IRQ I Interrupt request to the microprocessor, set Low for request and
        cleared when the status register is read.
HSYNC O Horizontal sync.
VBL I/O Vertical blanking identifies the period during which the
        display is blank while the CRT beam is in vertical retrace.
HBL O Horizontal blanking identifies the period during which the display
        is blank while the CRT beam is in horizontal retrace.
M/S I Master/Slave designates a device to be either a master or a slave
        unit. A master, so designated, feeds VBL and HBL to itself from its
        internal sync generator and also sends VBL and HBL out to the slave
        device if one exists. A slave, so designated receives VBL and HBL
        for its internal synchronization.
CLK I The clock input operates at a fixed frequency of 3.54 MHz. The
        duty cycle shall be 50% with 5% deviation.
R O The Red output is a chroma signal representing objects that are to be
        displayed in a read color.
G O The Green output is a chroma signal representing objects that are to
        be displayed in a green color.
B O The Blue output is a chroma signal representing objects that are to be
        displayed in a read color.
L O The Luminance output represents the ORed result of active patterns in the
        minor system, the major system, and the grid (if set grid bright is active)
BG O The Burst Gate defines the duration of the 4.43 MHz color reference signal
        required for generation of the composite color signal in external analog
        circuitry.
SND O The Sound output provides an audio driving signal to the external sound
        modulator.
STB I The position strobe input.
CX I Chip Expander. If there are 2 8245's in a system, LUM #2 is connected to
        CX #1 and LUM #1 is connected to CX #2. This allows status or overlaps
        between objects on different chips to be read by the CPU.
VCC I +5V supply.
VSS I Gnd.

8245 PINOUT

SUMMARY

The 8085 timings are more restrictive than the 8048 timings. Although the initial
game product will match an 8245 with an 8048, it is desirable to design the 8245 to
work with both the 8048 and the 8085. This will allow upwards compatibility with
the more powerful CPU and very probably will extend the product life of the 8245.
The following timings should allow the 8245 to work in either system.

READ CYCLE:

WRITE CYCLE:

References: “Standard Peripheral Timing for 8085 Bus”, April 20, 1976; 8048/8748/8035
<cropped> datasheet, September 1976

SYMBOL DESCRIPTION MIN MAX UNITS

tAL ......... Address valid before T.E. of ALE ... 50 NSEC
tLA ......... Address hold time after ALE ... 100 NSEC
tLL ......... ALE width ... 100 NSEC
tAC ......... Address valid to L.E. of control ... 150 NSEC
tLC ......... T.E. of ALE to L.E. of control ... 100 NSEC
tAD ......... Address valid to valid data out ... 400 NSEC
tRD ......... Data out delay from RD ... 150 NSEC
tRDF ......... Data bus float after RD ... 10 75 NSEC
tCC ......... Width of control ... 250 NSEC
tDW ......... Data in valid to T.E. of WR ... 150 NSEC
tWD ......... Data valid after T.E. of WR ... 0 NSEC
tCL ......... T.E. of control to L.E. of ALE ... 20 NSEC
tRV ......... T.E. of control to L.E. of next ... 300 NSEC
        control
tCA ......... Address hold after control ... 0 NSEC

NOTE: The 8245 will ignore the information on the data lines except for the cycles
       when overline RD or overline WR are active.

8245 ELECTRICAL SPECIFICATION

D.C. CHARACTERISTICS

TA = 0ºC to 70ºC; VCC = +5V ±5%; VSS = 0V

SYMBOL PARAMETER MIN. TYP. MAX. UNIT CONDITIONS

VIL* Input low voltage VSS-0.5 0.8 V
VIH* Input high voltage 2.0 VCC V
VOL Output low voltage 0.45 V IOL = 1.6mA
VOH Output high voltage 2.4 V IOH = -200µA
IIL Input leakage ± 20 µA (VSS + 0.45) ≤
        VIN ≤ VCC
ICC VCC current drain 200 mA
A.C. CHARACTERISTICS

TA = 0ºC to 70ºC; VCC = +5V ±5%; VSS = 0V

Timing measurements are made at the following reference voltages unless otherwise
noted:

     Input “1” = 2.0V, “0” = 0.8V
     Output “1” = 2.0V, “0” = 0.8V

Output loading consists of one TTL load and 50pF total external capacitance except
the system bus which is loaded by one TTL load and 100pF.
* Except CLK input which has VIL = 0.5 MAX VIH = 4.0 MIN and rise/fall time

Rise and fall times will be 200 NSEC or less. Rise and fall times will be measured
from 0.8V to 2.0V. RGB outputs occur within 25 nsec, of each other, luminance output
will occur 0 to 150 nsec, after RGB.

FUNCTIONAL SPECIFICATION

     The 8245 is organized as a group of subfunction blocks that communicate via
an internal bus with the I/O port. Most of the subfunctions are individually
addressable for the transfer of information with the controlling microprocessor.
These blocks may be categorized functionally as follows:

     1. Major display system
     2. Minor display system
     3. Grid display system
     4. Sound system
     5. Status and control circuits
     6. Sync generator

    The use of both major and minor display systems provides hardware parallelism
to circumvent the problem of concurrent objects. In general, the single major
system is used to display fixed objects, while the plurality of minor systems
similarly handles moving objects. In exceptional cases nonstrategic moving objects
may be placed in the major system but this should be avoided where accommodation is
provided by the minor systems. All objects in the major system are composed of
8 X 7 bit arrays,* while all objects in the minor system are composed of 8 X 8 bit
arrays. Larger objects are produced by concatenation of the basic arrays. All
major system objects start on even lines.

     The grid display system places a segment programmable grid in the background
of the display. Any grid segment may be either inserted or deleted programmatically
to produce a variety of arrays such as checkerboards, racetracks, mazes, and etc.
An additional feature allows vertical segments to be expanded horizontally and thus
provide illuminated square and rectangular areas.

     The sound system contains both a random noise generator as well as a programmed
sound section. The resulting signals may be combined digitally to produce special
effects such as gun shot sounds.

     The status and control circuits provide a message transfer mechanism between the
8245 and the microprocessor. Control messages sent from the microprocessor are
utilized within the control circuits. These messages determine the types of status
messages to be returned and also define certain key conditions associated with the
displayed objects. The status messages returned to the microprocessor from the 8245
provide information relative to the display that is used by the microprocessor for
input to the program.

* An 8 X 7 array is composed of 8 horizontal dots and (7 X 2) horizontal lines.

     The sync generator provides both sync and blanking signals for use internally
on the chip as well as an output for use by the accompanying TV modulator circuitry.
A color burst gate is also provided as an output for use by the modulator. The manner
in which the sync generator output signals are utilized is determined by the program
ming of the M/S input pin. A high level or ‘1’ input designates the Master mode and
causes the sync generator outputs to drive both internal circuitry abd to provide
outputs on the appropriate pins (HBL, VBL, CSY and BG). Conversely, a low level or
‘0’ input designates the Slave mode and allows the HBL and VBL pins to be used as
inputs which are then driven by another 8244 designated as a Master. In this later
case, both CSY and BG are derived from the Master 8244 along with HBL and VBL for
use by the external circuitry. A non interlaced sweep format is used, primarily,
to eliminate the objectionable effect known as “color crawl”. The resulting sweep
rates are close to Americal NTSC standards so that there will be no difficulty in
synchronization. For operation on European standards, the 8244 will be operated in
the Slave mode and appropriate signals will be supplied to it from external sync
circuitry.

MAJOR DISPLAY SYSTEM

     The purpose of the major display system is to position and select both specific
fixed objects and also non-colliding moving objects of a non-strategic nature. This
system can position a total of 28 objects in the static positioning mode1 and a
greater number in the dynamic positioning mode2. The positioning of each individual
object requires 15 bits of addressing information. All addressing is physically
relative to the upper left hand corner of the display field. The first 7 bits
specify the vertical position which can be on one of 121 even scanning lines in a
field. The remaining 8 bits specify one of 183 positions horizontally across the
screen. All objects in the major system are fixed in size.

     The major system is partitioned into a pair of groups, where each group is
optimized for different types of displays. This expedient allows a considerable
reduction in chip size without adversely affecting total function. Primarily, the
first group provides for alphanumberic or grouped object display by allowing each
CAM location to point to a character group of up to four arbitrarily selectable
objects. These objects have a fixed spacing at 16 clock intervals which allows
matching of object placement with the grid format. Thus, a single CAM location
may place up to four objects centered within the grid areas. For the purpose of
textual presentation, associated pairs of CAM locations may locate alphanumerics
in an interspersed fashion so as to provide adjacent characters. Alternatively,
any object spacing may be achieved either by programming appropriate blanks or
different starting locations.

1 The static positioning mode loads all object data during vertical blanking
   interval.

2 The dynamic positioning mode loads any or all object data during horizontal
   blanking interval.

     The first group uses four CAM locations to provide starting points for multiple
objects. Each group CAM location contains an additional 2-bit counter and thereby
is able to point to four LSS* locations. Thus, the first group controls the place-
ment and selection of 16 objects. If the fourth pattern is truncated all four
objects will be truncated to the height of the fourth.

     The second group within the major system provides for the placement of game
obstacles that are either fixed in location or may be movable within certain
restrictions. As movable objects, they should not be utilized as strategic elements
such as balls, bullets, race cars, etc. However, they do provide slow moving
obstacles such as covered wagons or other vehicles. In addition, these objects,
when moving, should be prevented from overlapping any other objects in the major
system as no means for identification by the microprocessor is available. This
nonoverlapping function is achieved by proper programming. Within this group there
is a one to one correspondence between a CAM location and a single displayed object.
Since there are 12 CAM locations in the second group, there are also 12 objects
that may be placed.

     The portion of the total CAM array that constitutes the major system points
to a total of 28 storage locations in the LSS. The information stored in the LSS
represents the location address of the associated pattern in the pattern ROM.
Rather than store the starting address of the desired pattern in the LSS, a two's
complement displacement is stored. This expedient allows a simple hardware
mechanism for sequencing through the consecutive addresses of ROM patterns as
they are encountered. The displacement represents the difference between the
starting address of the object pattern in ROM and the scanning line number in
the raster display. This may be simply stated as follows:
     LSS_N~=~ROM`object`Address - left [(VertiCam Data)_N over 2 right ]

     N = Object Number

     A single 9 bit adder is sufficient for accommodating all address sequencing
for the major system. The LSS must be able to store 9 bit displacements. The
sequence of events that takes place for the placement of an object pattern is
as follows: As a match occurs between the contents of the beam location counter
and the address stored in any particular CAM cell, a pointer enables an output
from the particular associated line number, obtained from the line counter,
and results in the address of the desired row of the object pattern in ROM.
If the full 8 X 7 pattern is desired, then the first match of the CAM causes
the above described procedure to produce the starting address of the object
pattern in ROM. As horizontal matches occur on successive scan lines, a
consequential incrementation of the ROM address occurs. An end of pattern
address is detected on every eighth address and terminates the presentation of
each particular object. There is no restriction as to whether a full 8 X 7 or
any portion of the pattern in the vertical dimension may be presented as a displayed
object. This flexibility allows the programmer to use fractions of object patterns
if it is desired to do so.

*LSS = Linear Select Store

     In addition to the 9 bit displacement in each location in the LSS, there is
provision for the storage of 3 color bits. These bits designate the primary
colors red, green, and blue. By the activation of more than one color bit
simultaneously, various hues are also produced.

     The following table presents a summary of the specifications for the major
system:

No. of
Simul Objects
CAM loc.
No. of
Simul Objects
Group

Group
No. of
Selectable
Objects *
Disp.
Bits in
LSS
No. of
Bits in
Hor. CAM
No. of
Bits in
Vert. CAM
No. of
CAM
Loc.
Attribute
Bits in
LSS
Object
Size

  1 4 7 8 4 16 64 9 3 8 dots wide
        14 lines high
  2 12 7 8 1 12 64 9 3 8 dots wide
        14 lines high

* There are 64 objects total, any of which can be selected by either Group.

MINOR DISPLAY SYSTEM

As a first order objective all strategic objects are selected and displayed by the
minor display system. In some games it may be useful to put fixed objects in the
minor system and there is no restriction that prevents this. There are four repli-
cated blocks within the minor system. Each block is autonomous in function and
provides for the placement of a single object. Each of these objects may collide
with each other or with objects in the major system. In either event, the minor
object is readily identifiable by the microprocessor so that immediate responsive
action may be taken.

Minor system objects are locatable by a portion of the overall CAM array, just as in
the major system. However, the similarity of the two systems ends in the signal
path beyond the CAM array. Each of the four CAM locations in the minor system is
dedicated and points to a singular block of object pattern bits located in RAM
storage. In contrast, the CAM locations in the major system can point to any of
the 64 objects stored in the pattern ROM. In addition, the mechanism for sequencing
through the rows of the pattern RAM's is different than that used in the major system.
In place of a singular adder as used in the major system, each minor system contains
its individual three bit counter. This counter is updated at the beginning of each
horizontal scan line. The decoding of the counter points to the proper location in
the pattern RAM. Thus, each dot row in an object is presented as the RAM locations
are sequenced. The RAM locations are loadable from the internal bus by a Write
operation of the microprocessor. The RAM has the capacity to store eight bytes
for each object thereby allowing an 8 X 8 object presentation. Associated with
each minor system is an Attribute Register whose contents are arranged as follows:

        7 6 5 4 3 2 1 0

        X X B G R D S X9

The Bits in this register are defined as follows:

Bit 0 – X9 is the ninth Bit in the horizontal address of the beam location. This
bit allows the beam location to be resolved to 140ns increments.

Bit 1 – The S or smoothing Bit allows a displacement of either the odd or even
count horizontal sweep lines in order to provide an improved appearance of objects
that visually rotate on the screen.

Bit 2 – The D or duration Bit determines whether an object will be presented in
normal size or if its x and y dimensions will be increased by a factor of two.

Bit 3 – The R Bit specifies whether the object contains a red component of color
display.

Bit 4 – The G Bit specifies whether the object contains a green component of color
display.

Bit 5 – The B Bit specifies whether the object contains a blue component of color
display.

Bits 6 and 7 – These bits are unspecified and exert no control.

The definition of the delay of dot rows within an object depends on Bits 0, 1,
and 2 as shown in the following table:

        Bit 2 Bit 1 Bit 0 Even Line Odd Line
        D S X9 Delay (ns) Delay (ns)

        0 0 0 0 0
        0 0 1 140 140
        0 1 0 140 0
        0 1 1 0 140
        1 0 0 0 0
        1 0 1 280 280
        1 1 0 280 0
        1 1 1 0 280

GRID DISPLAY SYSTEM

The grid display consists of an array of nine enclosed areas horizontally and
eight areas vertically. Each line segment between the nodes of the array is
individually controllable so that it may be presented or be inhibited.

A full array, consisting of all segments present, is created by combining nine
complete horizontal display bars with ten complete vertical display bars. Each
horizontal bar consists of nine concatenated bar segments, while a vertical bar
consists of eight concatenated bar segments. Each horizontal bar on the TV
screen is composed of three consecutive horizontal scan lines, while adjacent
bars are spaced by 21 horizontal scan lines. A vertical bar is made up of a
column of dot groups. Each dot group is programmable to consist of either two
or sixteen clock intervals (3.54Mhz) in width*. A conventional grid utilizes
two clock intervals while large area clock arrays, such as checkerboards,
utilize sixteen clock intervals. The spacing between adjacent vertical bars
is fourteen clock intervals. Thus, wide vertical bar segments that are adjacent,
appear to be continuous displayed areas. The grid is centered vertically on the
TV screen by allowing the first or top horizontal bar to start on the 24th
horizontal scan line relative to the end of vertical blanking (VBL). Similarly,
horizontal centering is accomplished by allowing the first or left-most vertical
bar to start on the 10th clock cycle from the end of horizontal blanking (HBL).

A programmable feature allows the grid to be augmented by the addition of a
dot matrix. In this case the dots appear at a physical placement on the TV
screen, where otherwise the intersection of the horizontal and vertical bars
would appear. The dots are composed of three horizontal scan line segments
that have a width equivalent to two clock cycles. Since, a full array of dots
is always presented, no segment programming requirement exists for dot arrays,
although segments and dots can simultaneously be displayed.

An additional programmable feature allows the grid display, or any of its
previously described subsets, to be either presented or inhibited on the
TV screen.

The upper left hand corner of the grid has program coordinates (Y,X) = (13H,0BH).
The observed position on the screen will be (Y,X) = (18H,18H).

* Horizontal displacement on the TV screen is directly proportional to time.

SOUND SYSTEM

The sound system generates a duty cycle modulated square wave from which an audio
signal is extracted by means of an external low pass filter. The control of the
duty cycle is effected by information that is transferred from the microprocessor
to the 8245. This information consists of triple byte groups that determine the
audio frequency and an accompanying 4 bits that determine volume.

The triple byte groups are loaded into three-eight bit shift registers located
on the 8245. Each byte in the group is loaded sequentially into its respective
register during a load interval. All three bytes are loaded in between conse-
cutive shift clock pulses. The concatenation of the three registers results
in a 24 bit string that is shifted out by this shift clock. The resulting
serial pattern of ones and zeroes contains a fundamental band of frequency
components that lie in the audio range. This particular signal is further
“chopped” by a higher frequency that is a multiple of the shift clock. By
duty cycle modulation of this “chopping” signal, the amplitude of the audio
component is varied. There are four control bits that are used to control the
audio level. These bits are loaded into a four bit down counter that is shifted
by the high frequency shift clock. The resulting output is ANDED with the output
from the three concatenated shift registers to produce the composite audio output.
In addition to the four volume control bits, three other control bits are used
to augment the overall operation of the sound system. A noise enable bit enables
a feedback path in the output eight bit shift register, in the 25 bit shift path
to produce the noise component. Simultaneously, the noise is added to the audio
component that is progressing down the shift register.

The shift frequency for the register may be varied between two values by another
control bit. This expedient allows low audio frequencies to be produced with
fewer refresh cycles from the microprocessor than for high frequencies thus, re-
ducing the load on the processor.

For the reproduction of certain audio tones that are subharmonically related to
the shift clock, the need for microprocessor refresh is totally eliminated by
recirculation of the 24 bit shift path.

The format of the sound control word is described below:

        7 6 5 4 3 2 1 0

        EN X S N V3 V2 V1 V0

Bits 0 – 3 – Volume Bits, collectively as a 4 bit word, these bits define the
output audio level.

Bit – 4 – Noise Enable; controls noise generation and mixing with the audio
signal. Bit 4 = 1, noise on; Bit = 0, noise off.

SOUND SYSTEM

Bit 5 – Shift Frequency; determines frequency of shift clock.
Bit 5 = 1, f = 3933Hz. Bit 5 = 0, f = 983Hz.
(3933Hz~=~H over 4~=~15,734 over 4`;~983Hz~=~H over 16~=~15,734 over 16)

Bit 7 – Enable sound; 0 = No sound, 1 = sound.

For those modes of operation requiring sound refresh data from the microprocessor,
an interrupt is generated each time that the 24 sound bits have been shifted through
the three eight bit shift registers. A 5 bit counter set to module 24 counts shift
clocks and determines when the interrupt should occur.

The sound shift registers, volume counter and sound control word register are all
individually addressed by the microprocessor for the purpose of loading data. The
address of these elements is shown under the topic of “Address Structure”.

CONTROL AND STATUS

The control over various operational parameters on the chip is effected by the
bits in the control word that is written into the control register by the
microprocessor. The bits in the control word are defined as follows:

Bit 0 – Enable Horizontal Interrupt, generates an interrupt 20 µs in advance of
the occurrence of horizontal blanking. This advance notice to the microprocessor
allows a sufficient interval for the reading of the status information so that
appropriate control can be exerted during the horizontal blanking interval.

Bit 1* - Forced Position Strobe, allows the freezing of the beam location infor-
mation in the X-Y position registers so that the microprocessor can locate the
beam at any time. Bit 1 = 1 strobes beam location to X-Y registers. Bit 1 = 0
disables strobe internal, but external strobe through position strobe Pin can
still take place.

Bit 2 – Enable Sound Interrupt, allows an interrupt to be generated whenever the
sound register needs new data. Bit 2 = 1 enables sound interrupt, Bit 2 = 0
disables sound interrupt.

Bit 3 – Enable Grid, allows two luminance levels of the grid. If the bit is a 0,
the luminance signal is inhibited during grid information intervals. If the Bit
is a 1, the luminance signal is active during grid information intervals.

Bit 4 – Enable External Overlap Interrupt, allows an interrupt upon detection of
an overlap, when more than one 8245 exists in a system.

Bit 5 – Enable Display, allows objects to be displayed. Bit 5 = 1 enables display;
Bit 5 = 0 disables objects. The purpose of this bit is to allow the µP to write
new data to the 8245 when the display is part way through a display field. It
is the responsibility of the software to disable the display only when there are
no active patterns being displayed.

Bit 6 – Dot Enable, allows the presentation of a dot array in addition to the
grid array. The dots appear at the intersection of the horizontal and vertical
lines in the grid format. Bit 6 = 1 enables dots; bit 6 = 0 enables normal grid.

Bit 7 – Grid Segment Width, allows the selection of narrow or wide vertical
segments in the grid. Bit 7 = 1 enables wide segments; bit 7 = 0 enables narrow
grid.

The color of the grid and background is determined by the data stored in the
Color Latch. Also by setting the Enable Grid bit to '0' the grid can be turned
off and the grid RAM can be used for other data storage. The bits in the Color
Latch are defined as follows:

*The “or” of STB and Force Position Strobe will cause X-Y reg to follow the
 BLC. A falling edge on the OR output will freeze the BLC. The reg will
 remain frozen until after the x-register is read. This strobe will not cause
 false data to be loaded into latch (synchronized on 0 edge, when BLC is not
 changing).

Bit 0 – Grid Color Blue Bit 4 – Background Color Green
Bit 1 – Grid Color Green Bit 5 – Background Color Red
Bit 2 – Grid Color Red Bit 6 – Set Grid Bright
Bit 3 – Background Color Blue

CONTROL AND STATUS

The Enable Overlap register allows for selectable masking of overlaps. When a
bit in the Enable Overlap register is a '0' the overlap of that object with
any other object will not set the bits for the other objects in the Overlap
Status register. The bit pattern is as follows:

Bit 0 – Minor System 0 Bit 4 – Vertical Grid
Bit 1 – Minor System 1 Bit 5 – Horizontal Grid and dots
Bit 2 – Minor System 2 Bit 6 – External Chip
Bit 3 – Minor System 3 Bit 7 – Major System

The Overlap Status register stores the coincidences as they occur on the screen.
Whenever two or more objects are simultaneously displayed the bits for both
objects are set unless the Enable Overlap register has those bits masked. The
External Chip overlap corresponds to the Signal on the 'CX' Pin. The bit pattern
is the same as that of the Enable Overlap Register above. This register is reset
when read.

The Control Status Word is used to determine the chip status and interrupt sources.
The bit pattern is as follows:

Bit 0 – Horizontal Status – Starts 20 µs before Horizontal blank starts. Ends 5 µs
before Horizontal blank ends.

Bit 1 – Position Strobe Status – Status of X-Y Register strobe '1' = Follow Beam
Location Ctr, '0' = latched. (See note on page 14)

Bit 2 – Sound Needs Service – Sound register empty

Bit 3 – Vertical Status = Vertical Blanking

Bit 4 – N/C

Bit 5 – N/C

Bit 6 – External Chip Overlap Interrupt – Set when an overlap occurs with signal
on 'CX' Pin.

Bit 7 – Major System Overlap – Set when the chip attempts to load major system
shift register if shift register already has one. The status register bits 2, 6
and the interrupt flip flop are cleared by reading the status reg. The overlap
status register is cleared when read.

SYNC GENERATOR

The sync generator operates as a non-addressable autonomous circuit block within
the 8245. As such, it provides a source for synchronizing signals both for
internal use by the 8245 circuitry and for transmission to external circuitry.
Externally the signal becomes processed with the color, luminance, and sound
signals and ultimately results in synchronization of the associated TV receiver.

The manner in which the signals are utilized is determined by the mode in which
the 8245 operates in a particular configuration. In a small system, utilizing
a single 8245, it is operated in the Master Mode. The signals from the sync generator
drive both the display circuitry on the 8245 and also exit the chip, via appropriate
pins, to drive the external circuitry. The external logic and the 8245 sync logic
together generate sync signals compatible with CCI standards.

In larger system configurations, where the need for more than one 8245 exists,
a single 8245 is designated the Master, as previously described. In addition,
one or more 8244's are used as Slave Mode devices by connecting their M/S pins
to Vss. The sync generator on a Slave Mode device is free to run but the output
is not utilized outside the chip.

In Master Mode operation the sync generator signals used internally by the 8245
are horizontal blanking (HBL) and vertical blanking (VBL). Correspondingly,
these two signals provide outputs along with horizontal sync (HSYNC) and color
burst gate (BG). In Slave Mode operation the 8244 received only HBL and VBL
from a Master Mode 8245.

The sync generator in conjunction with external logic provides non-interlaced
synchronizing signals. It operates from a frequency of 3.54 Mhz. This clocking
signal is divided by a factor of 227.0 in order to obtain the horizontal line
frequency of 15,625 Hz.

In conjunction with external circuitry the horizontal line frequency is divided
by a factor of 313 or 312 to produce the vertical sync frequency of 49.92 Hz.
In the following timing diagrams, those signals shown under Horizontal Timing are
reproduced at the 15,625 Hz rate, while the signals shown under Vertical Timing
are reproduced at the 49.92 Hz or 50.08 Hz rate. Horizontal Blanking Burst Gate,
and Horizontal Sync are generated during all portions of the vertical timing
sequence. Vertical Interrupts are not generated within the 8245, although the
vertical status bit is set during Vertical Blanking.

SYNC GENERATOR

ADDRESS STRUCTURE

The subfunction blocks within the 8244 may be individually addressed for the
writing and in some cases, the reading of data. The addressing structure of
these blocks is shown below:

        CAM AND LINEAR SELECT STORE

        ADDRESS SUBFUNCTION

  Bit: 7 6 5 4 3 2 1 0

        0 Object 0 0 LINE CAM (Y CAM)

        0 Number 0 1 DOT CAM (X CAM)

        0 1 0 LSS BITS 0-7
        0 1 1 LSS BITS 8-11

  Note: For the Minor System LSS Bits 0-7 are attribute bits stored in the
        Attribute register.

ADDRESS STRUCTURE

        MINOR SYSTEM PATTERN RAM

        ADDRESS SUBFUNCTION

      Bit: 7 6 5 4 3 2 1 0 PATTERN RAM

        1 0 0| | |

        OBJECT PATTERN
        NUMBER RAM LINE

        NUMBER

        MISCELLANEOUS REGISTERS

        ADDRESS SUBFUNCTION

      Bit: 7 6 5 4 3 2 1 0

        1 0 1 X 0 0 0 0 CONTROL
        0 0 0 1 CONTROL STATUS
        0 0 1 0 OVERLAP STATUS AND OVERLAP ENABLE
        0 0 1 1 COLOR LATCH
        0 1 0 0 Y REGISTER
        0 1 0 1 X REGISTER
        0 1 1 0 NA
        0 1 1 1 SOUND 0
        1 0 0 0 SOUND 1
        1 0 0 1 SOUND 2
        1 0 1 0 SOUND STATUS

      GRID

        ADDRESS SUBFUNCTION
      Bit: 7 6 5 4 3 2 1 0

        1 1 0 0 HORIZONTAL SEGMENTS 0 to 7,

        1 1 0 1 column HORIZONTAL SEGMENTS 8
        1 1 1 0 number VERTICAL SEGMENTS

      READ AND WRITE CAPABILITY:

      READ/WRITE: ALL CAM
        ALL LINEAR STORE EXCEPT MINOR SYSTEM
        GRID RAM
        MINOR SYSTEM PATTERN RAM
        CONTROL REG.
        SOUND STATUS REG.

ADDRESS STRUCTURE

READ ONLY: X-REG
        Y-REG
        OVERLAP STATUS REG
        CONTROL STATUS REG

WRITE ONLY: MINOR SYSTEM LINEAR STORE (ATTRIBUTE REG)
        COLOR LATCH
        ENABLE OVERLAP
        SOUND REGS 0, 1, 2

ADDRESS STRUCTURE

The addressable function block structure may be shown by means of an overview
address map as follows:

ADDRESS STRUCTURE

A more detailed breakdown of the addressable function block is shown as
follows:

ADDRESS STRUCTURE

The addressing of the individual memory sections within the Minor and Major
systems is shown as follows:

MINOR SYSTEMS

  ADDRESSING

        SYSTEM NO. Y CAM X CAM LSS

        0 00H 01H 02H
        1 04 05 06
        2 08 09 0A
        3 0C 0D 0E

WORD FORMATS

  Bits 7 6 5 4 3 2 1 0

Y CAM MSB LSB
X CAM MSB 2ndLSB
LSS x x B G R D S X9

PATTERN RAM Address

SYSTEM NO. ADDRESS

   0 80H Line 1
        81 Line 2
        87 Line 8
   1 88 Line 1
        Line 2

        8F Line 8
   2 90 Line 1
        Line 2

        97 Line 8
   3 98 Line 1
        Line 2
        9F Line 8

   RAM WORD FORMAT

     Bits 7 6 5 4 3 2 1 0

        last out 1st out

MAJOR SYSTEMS

ADDRESSING
        LSS #1 LSS#2 LSS #3 LSS #4
   SYSTEM NO. Y CAM X CAM A B

      0 10 11 12,13
      1 14 15 16,17
      2 18 19 1A,1B
      3 1C 1D 1E,1F
      4 20 21 22,23
      5 24 25 26,27
      6 28 29 2A,2B
      7 2C 2D 2E,2F
      8 30 31 32,33
      9 34 35 36,37
      10 38 39 3A,3B
      11 3C 3D 3E,3F
      12 40+44+ 41+45+ 42.43 46,47 4A,4B 4E,4F

        48+4C 49+4D
      13 50+54+ 51+55+ 52,53 56,57 5A,5B 5E,5F
GROUP

MAJOR
        58+5C 59+5D
      14 60+64+ 61+65+ 62,63 66,67 6A,6B 6E,6F
        68+6C 69+6D
      15 70+74+ 71+75+ 72,73 76,77 7A,7B 7E.7F
        78+7C 79+7D

WORD FORMATS

        Bits 7 6 5 4 3 2 1 0

    Y CAM MSB LSB
    X CAM MSB LSB
    LSS (0-7) 2ndMSB LSB
    LSS (8-11) B G R MSB

ADDRESS STRUCTURE

The addressing of the Grid elements is shown relative to the overall grid display as
follows:

- missing -